## Slide 1: OCF Core Technology, aka IoT platform OCF 1.0
June 2017
JinHyeock Choi

## Slide 2: Contents
IoT overview
  Core technologies
OCF Architecture
  Functional Block Diagram
OCF Framework
  OCF common features
OCF components & procedures
  Resource, Resource Type, Device
  RESTful Transaction

## Slide 3: Specification & Resource Type location
OCF Specifications: OCF 1.0
  https://openconnectivity.org/developer/specifications
Resource Type Definitions
  Core Resources:
    https://github.com/openconnectivityfoundation/core
  Bridging Resources:
    https://github.com/openconnectivityfoundation/bridging
  Security Resources:
    https://github.com/openconnectivityfoundation/security-models
  Vertical Resources and Derived Models:
    https://oneiota.org
Presentation

## Slide 4: Specification Location
Where can I find the specifications and Resource Type definitions?
OCF Specifications:
Add public links here
Resource Type Definitions
Core Resources: https://github.com/openconnectivityfoundation/core
Bridging Resources: https://github.com/openconnectivityfoundation/bridging
Security Resources: https://github.com/openconnectivityfoundation/security-models
Vertical Resources and Derived Models: https://oneiota.org/documents?filter%5Bmedia_type%5D=application%2Framl%2Byaml

## Slide 5: Internet of Things
Cyber Physical System
Real World Internet
Ubiquitous Computing
M2M
Web of Thing
Internet of Everything

## Slide 6: Internet
User
Human
Cyber World
Cyber World open to Human
Digital

## Slide 7: Internet of Things?
User
Physical World
Human
Cyber World
Cyber & Physical World integrated & open to Human
Cyber World open to Human
Digital
Physical

## Slide 8: RESTful Architecture Style
Client
Server
Request
Response
CRUD & N operation
Resource (representation)
Resource (representation)
Addressable resources
A uniform, constrained interface
Representation based manipulation
Communicate statelessly
Hypermedia State Engine
REST Architecture Style
{
"n": "myRoomTemperature",
"rt": "oic.r.temperature",
"if": "oic.if.a",
"id": "example_id_xyz",
"temperature": 23,
"units": "C",
"setValue": 25
}
Physical entity
Entity handler
RESTful Architecture (Representational State Transfer)
  Resource based operation
    Real world ‘entity’ is represented as ‘Resource’
  Resource manipulation via Request/ Response: CRUDN

## Slide 9: (conceptual) IoT Architecture & Procedures
User
Device
Sensor
Sensor
Actuator
Gateway
Service Server
Actuator

## Slide 10: (conceptual) IoT Architecture & Procedures
User
Device
Sensor
Sensor
Actuator
Gateway
Service Server
Actuator
Monitoring with sensors
0. Event occurrence
1. Request sensor for data
2. Response with data

## Slide 11: (conceptual) IoT Architecture & Procedures
User
Device
Sensor
Sensor
Actuator
Gateway
Service Server
Actuator
Monitoring with sensors
0. Event occurrence
1. Request sensor for data
2. Response with data
3. Notify without Request

## Slide 12: (conceptual) IoT Architecture & Procedures
User
Device
Sensor
Sensor
Actuator
Gateway
Service Server
Actuator
Controlling with actuators
0. Event occurrence
1. Request actuators for state transfer
2. Actuator action
3. Response with state information

## Slide 13: (conceptual) IoT Architecture & Procedures
User
Device
Sensor
Sensor
Actuator
Gateway
Service Server
Actuator
Controlling & Monitoring
with sensor & actuator

## Slide 14: Main IoT challenges
User
Device
Sensor
Sensor
Actuator
Gateway
Service Server
Actuator
Networked Embedded Device
Connectivity
IoT Network
IoT Core Framework
Big Data Analysis
UX
IoT Security
세부 설명 추가

## Slide 15: RESTful Architecture Style
Client
Server
Request
Response
CRUD & N operation
Resource (representation)
Resource (representation)
Addressable resources
A uniform, constrained interface
Representation based manipulation
Communicate statelessly
Hypermedia State Engine
REST Architecture Style
{
"n": "myRoomTemperature",
"rt": "oic.r.temperature",
"if": "oic.if.a",
"id": "example_id_xyz",
"temperature": 23,
"units": "C",
"setValue": 25
}
Physical entity
Entity handler
RESTful Architecture (Representational State Transfer)
  Resource based operation
    Real world ‘entity’ is represented as ‘Resource’
  Resource manipulation via Request/ Response: CRUDN

## Slide 16: Logical organization: 3 part approach
Entity Handler
Entity (e.g. HW Sensor)
Abstraction
[OIC Concepts & Architecture Review, Ravi Subramaniam]
Communication and Interoperability
(Protocol processing
& Messaging)
Resource model and organization
(Declarative)
Device abstraction (entity handler)
(Imperative)
RESTful transaction
Abstraction
Resource model

## Slide 17: Logical organization: 3 part approach
[OIC Concepts & Architecture Review, Ravi Subramaniam]
Resource Type
Resource
/s/hm/data
Relative URI
/192.168.1.1/s/hm/mgmt
Fully-qualified URI
Resolution: I
Range: I
Name: S
Time: UT
Rate: F
Name: S
Resource Interface
Resource Model
Abstraction
Communication and Interoperability
(Protocol processing
& Messaging)
Resource model and organization
(Declarative)
Device abstraction (entity handler)
(Imperative)
RESTful transaction
Abstraction
Resource model
OIC Server
Binding
Resource Address
Resource
Entity Handler
Entity (e.g. HW Sensor)

## Slide 18: Logical organization: 3 part approach
[OIC Concepts & Architecture Review, Ravi Subramaniam]
OIC Client
CoAP
Device:
“Wrist Band”
Request
Response
Time: 11:30
Rate: 80
Name: Ravi HR
Representation
URI: /s/hm/data
GET
Protocol
Servlet
RESTful transaction
Resource Type
Resource
/s/hm/data
Relative URI
/192.168.1.1/s/hm/mgmt
Fully-qualified URI
Resolution: I
Range: I
Name: S
Time: UT
Rate: F
Name: S
Resource Interface
Resource Model
Abstraction
Communication and Interoperability
(Protocol processing
& Messaging)
Resource model and organization
(Declarative)
Device abstraction (entity handler)
(Imperative)
RESTful transaction
Abstraction
Resource model
OIC Server
Binding
Resource Address
Resource
Entity Handler
Entity (e.g. HW Sensor)

## Slide 19: Logical organization: 3 part approach
Resource Type
Entity Handler
Entity (e.g. HW Sensor)
Resource
Resource
/s/hm/data
Relative URI
/192.168.1.1/s/hm/mgmt
Fully-qualified URI
Binding
Resource Address
OIC Server
OIC Client
CoAP
Device:
“Wrist Band”
Request
Response
Resolution: I
Range: I
Name: S
Time: UT
Rate: F
Name: S
Time: 11:30
Rate: 80
Name: Ravi HR
Representation
URI: /s/hm/data
GET
Protocol
Servlet
Resource Interface
RESTful transaction
Resource Model
Abstraction
[OIC Concepts & Architecture Review, Ravi Subramaniam]
Communication and Interoperability
(Protocol processing
& Messaging)
Resource model and organization
(Declarative)
Device abstraction (entity handler)
(Imperative)
RESTful transaction
Abstraction
Resource model

## Slide 20: IoT Protocol Stacks
20
OPEN CONNECTIVITY FOUNDATION MEMBER CONFIDENTIAL INFORMATION
DMC R&D Center ⓒ 2013 SAMSUNG Electronics Co.
6loWPAN
IPv6
6tisch
6lo
RFC 4862
RFC 4861
16ng
RFC 6459
ETSI TS102859
IEEE 802.3 Ethernet
IEEE 802.11 WiFi
IEEE 802.15.1 Bluetooth
IEEE 802.15.7 VLC
IEEE 802.15.4 Zigbee
IEEE 1901.2 PLC
IEEE 802.11 p C2C-CC
IEEE 802.16 WiMAX
Cellular 3GPP LTE
IP over Foo (PLC, VLC)
Geo-Networking
Energy Efficient Protocol
Delay Tolerant Transport
RPL
6light
homenet
eman
Ad-hoc VANET
Proxy/ Gateway
MIB
TCP
UDP
QUIC
SCTP
RTP
ICMP
Access Control
AAA
EAP
DIAMETER
SSL/TLS
HTTP/ HTTPS
CoAP
MQTT
XMPP
DDS
DNS
Resource Abstract
URI/ ID
Meta data /Link
Resource Representation
Attributes
Structure/ Org
Resource Rendezvous
Virtual BUS
Service Discovery
Resource Manipulation
CRUDN
Sensing Acting
Physical
Network
Service
Platform
Service Profile 1
(Connected Health)
Service Profile 2
(Connected Edu)
Service Profile 3
(Connected Car)
Service Profile 4
(Connected Retail)
Service Profile 5
(Smart City)
SIP
SSDP
Model/ JSON

## Slide 21: Internet & IoT layer comparison
sensing, acting
OCF, oneM2M, CoAP
DTN
v6
6LowPAN…
WiFi, BLE, VANET...
fiber, radio, light...
email, web, phone...
WWW, HTTP, URL
TCP UDP
IP
ND, ARP…
Ethernet, sonet...
copper fiber radio...
Internet
IoT
Network
[from Internet Hourglass model
by Steve Deering]
Service layer

## Slide 22: (background) Service layer – oneM2M
oneM2M Layered Model
Common Services Functions
[From TS0001 Functional Architecture, oneM2M]

## Slide 23: (background) Service layer – oneM2M
[Cisco presentation at IoT World Forum 2013]

## Slide 24: (background) Service layer – oneM2M
[Cisco presentation at IoT World Forum 2013]
oneM2M Layered Model
Network
Service layer

## Slide 25: OCF Functional Block Diagram
{
"n": MyRoomLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a“],
"id": "b.switch_TF38_3",
"value": "true"
}
Transport
Networking
L2 Connectivity
Application profiles
Connected Health
Smart Home
Automotive
Retail
OCF Framework
ID & Addressing
Resource model
CRUDN
Messaging
Discovery
Device management
Security
Group management
Bridging
Streaming(?)
Vertical profile
Common
IoT functions or
OCF Core features,
IoT Platform(?)

## Slide 26: OCF Functional Block Diagram
Transport
Networking
L2 Connectivity
Application profiles
Connected Health
Smart Home
Automotive
Retail
OIC Framework
ID & Addressing
Resource model
CRUDN
Messaging
Discovery
Device management
Security
Group management
Bridging
Streaming(?)
CoAP, HTTP
TCP, UDP, DTN
Homenet, Anima
URI, UUID, IPv6
IPv6, 6lo, geonet
mDNS, DNS-SD
IBE, DTLS/TLS
oneM2M TS0001, ooo4
XMPP, MQTT
BT/ BLE, 802.15.4, 802.11p
Smart Object

## Slide 27: OCF Functional Block Diagram: WG/TGs
Transport
Networking
L2 Connectivity
Application profiles
Connected Health
Smart Home
Automotive
Retail
OCF Framework
ID & Addressing
Resource model
CRUDN
Messaging
Discovery
Device management
Security
Group management
Bridging
Streaming(?)
Smart Home TG
Core Framework TG
Security WG

## Slide 28: OCF Functional Block Diagram: WG/TGs
Transport
Networking
L2 Connectivity
Application profiles
Connected Health
Smart Home
Automotive
Retail
OCF Framework
ID & Addressing
Resource model
CRUDN
Messaging
Discovery
Device management
Security
Group management
Bridging
Streaming(?)
Smart Home Project
Architecture TG
Security WG
Automotive Project
Healthcare Project
BLE-GATT
Project
Cloud support (?)
CoAP Native Cloud Project
Bridging TG
JOOE Project
WiFi Easy
Setup Project
애니메이션

## Slide 29: OCF Framework: IoT Platform(?)
Transport
Networking
L2 Connectivity
Application profiles
Connected Health
Smart Home
Automotive
Retail
OCF Framework
ID & Addressing
Resource model
CRUDN
Messaging
Discovery
Device management
Security
Group management
Bridging
Streaming(?)

## Slide 30: OCF Framework: IoT Platform(?)
OCF Framework
Resource model
CRUDN
Device management
Group management
Bridging
Streaming
Messaging
Security
ID & Addressing
Transport
Networking
L2 Connectivity
Discovery
Application profiles
Connected Health
Smart Home
Automotive
Retail

## Slide 31: OCF Framework – IoT Platform?
OCF Framework
Group management
Bridging
Streaming
Device management
Security
Discovery
Messaging
ID & Addressing
CRUDN
Resource model
Identifier & locator for OCF entities with resolution scheme
Realizing CRUDN with transfer protocol (e.g., CoAP, HTTP, MQTT, DDS)
A way to construct Resource with attributes, Resource Type & Link.
Create, Retrieve, Update, Delete & Notification of Resource with generic Request & Response.
Manage device capability, configuration, monitoring and life cycle management.
Onboarding, Authentication, Authorization & Access control
Finding relevant device & service information. Pull or Push based & Direct & Indirect
Manage group & collective group activity, Group/ Scene/ Script/ Rule
Intermediate or translate between different echo, protocols. Bridging with Virtual entity with synchronization
Deliver data flow with QoS constraints.

## Slide 32: Core features & issues
Status
Core features | Sub-items | Status | Issues
ID & Addressing | Entity to identify: Resource, Device, App, User? |  | Define entities to identify Define identifier/Name per entity Identifier format: URI (URN+URL) Alignment with SHP, MSC, Mobile Present a resolution scheme
 | IDs per an entity: URI = URN + URL |  | 
 | ID format: UUID, URI? |  | 
 | Resolution scheme |  | 
Resource model | Resource terms: attributes, interface… |  | Clarify resource terms & rules Common resource & attributes Align with SHP or existing resource standard (oneM2M)
 | Resource structure: Link, Colleciton |  | 
 | Common resource & attributes |  | 
CRUDN | Generic Request & Response format |  | Parameters for REQ & RES Generic procedure (Notification)
 | CRUDN procedures with Request & Response |  | 
Discovery | Local: mDNS, or CoAP based |  | Multiprotocol: mDNS vs CoAP discovery Advance remote discovery Define a registration standard Term: Search & Advertisement (?)
 | Remote: TBD |  | 
 | Registration |  | 
 | Unsolicited (Search & Advertisement) |  | 
Messaging | CoAP, HTTP, MQTT |  | REST transaction with MQTT Multi-protocol: CoAP & MQTT CoAP over BT/ BLE
 | Non-IP support (CoAP over BT./BLE) |  | 
Streaming | Uni-directional streaming(?) TBD |  | Streaming with REST model
Device mgmt | On boarding, ii) configuration, iii) device monitoring & iv) diagnostics |  | OMA LWM2M? Resource model conflict?
Group mgmt | Collection with collective action |  | Align with open source
Protocol bridge | CoAP to Foo bridge(?) |  | Align with open source & ii) spec item?
Security | Provisioning, Authentication, Access Control |  | Align with ID & Addressing
mature
developing
Not started

## Slide 33: Current status
Status
Spec items | Sub-items | Status | Issues
ID & Addressing | ocf URI |  | No resolution scheme specified
Resource model | Resource, Properties, Resource Type |  | Collection CRUDN unspecified Interface still unclear (i.e. Interface as filter) Query needs further specification
 | Link & Collection |  | 
 | Interface |  | 
 | Query |  | 
CRUDN | CRUDN procedures with generic REQ & RES |  | Parameters for REQ & RES
Discovery | CoAP based discovery (Endpoint, Resource) |  | Random delay for CoAP multicast RD selection & publishing needs elaboration
 | Resource directory |  | 
Messaging | coap |  | CoAP over TCP needs further works Version options number assignment
 | coap+tcp |  | 
 | Versioning & Content-Format negotiation |  | 
Device mgmt | On boarding & Provisioning, ii) configuration, iii) Diagnostics & maintenance |  | On boarding & Provisioning in SecWG Configuration in 11.2 with oic.wk.con Maintenance in 11.5 with oic.wk.mnt Is it adequate?
Group mgmt | Group/Scene/Script/Rule |  | Only scene specified
Bridging (?) | Endpoint |  | 
 | Introspection |  | /oic/res swagger(?)
mature
developing
Not started

## Slide 34: Spec items – OCF Amsterdam
Spec items | Sub items | Needs | Person | Issues
Resource model | Interface (1059) |  | Michael | Interface as a filter Collection (CRUDN) “rt” query, query extension (“di”, “ins”), multi-query Representing complicated devices with Collection (Car) More elaborate actuation scheme (?form)
 | Collection (1058) |  | Michael | 
 | Query (1316, 1317) |  | Michael/Jin | 
 | Composite device (1057) |  | Michael | 
 | Actuation pattern (1213) |  | Michael | 
Discovery | Resource directory (1060) |  | Jin | RD selection, Resource publish/update/delete (PATCH?) Resolution scheme with mDNS(?) Periodic CoAP multicast(?)
 | Periodicity of CoAP multicast discovery (1274) |  | Ricahrd | 
 | mDNS based discovery |  | Ram(?) | 
Messaging | Pubsub (1537) |  | Jieun | Pubsub with IETF standard CoAP over TCP with IETF standard PATCH with IETF standard
 | Keep alive (1506) |  | Jieun/Richard | 
 | CoAP over TCP (1545) |  | Jieun/Richard | 
 | PATCH (1140) |  | Mark | 
Streaming | Uni-directional streaming(?) |  | ? | Streaming with REST model, AV solutions (from UPnP WG) (?)
Device mgmt | Filed updatability (1332) |  | Richard | 
Group mgmt | Scene/ Script/ Rule |  | Mark/Clarke | Smart Home Project(?)
Bridging | Intermediary |  | ? | 
 | AllJoyn Notification Interface (1173) |  | Michael | 
 | AllJoyn ControlPanel Interface (1174) |  | Michael | 
Security | Privacy (1050) |  | Dave | New Auth scheme & Re-direct
Needs indicates the existence of the requirement from product implementation.

## Slide 35: (tentative) OIC protocol stack
Smart Device
APP |  |  |  |  |  |  | 
REST |  |  |  |  |  |  | 
HTTP | MQTT | XMPP | DDS | RTP | CoAP | mDNS | SSDP
TCP |  |  |  | UDP |  |  | 
IPv4/ IPv6 |  |  |  |  |  |  | 
L2 Connectivity |  |  |  |  |  |  | 
Thin device (IP)
APP |  |  | 
REST |  |  | 
CoAP | mDNS | SSDP | MQTT
UDP |  |  | 
IPv4/ IPv6 |  |  | 
L2 Connectivity |  |  | 
Thinner device (non-IP)
APP Profile + (CoAP?) | 
GAP, GATT | 
SMP | ATT
L2CAP | 
Link Layer | 
BT Baseband + RF | 
APP Profile + (CoAP?) | 
GAP, GATT | 
SMP | ATT
L2CAP | 
Link Layer | 
BT Baseband + RF | 

## Slide 36: (tentative) OIC protocol stack
Smart Device
APP |  |  |  |  |  |  | 
REST |  |  |  |  |  |  | 
HTTP | MQTT | XMPP | DDS | RTP | CoAP | mDNS | SSDP
TCP |  |  |  | UDP |  |  | 
IPv4/ IPv6 |  |  |  |  |  |  | 
L2 Connectivity |  |  |  |  |  |  | 
Thin device (IP)
APP |  |  | 
REST |  |  | 
CoAP | mDNS | SSDP | MQTT
UDP |  |  | 
IPv4/ IPv6 |  |  | 
L2 Connectivity |  |  | 
Thinner device (non-IP)
APP Profile + (CoAP?) | 
GAP, GATT | 
SMP | ATT
L2CAP | 
Link Layer | 
BT Baseband + RF | 
APP Profile + (CoAP?) | 
GAP, GATT | 
SMP | ATT
L2CAP | 
Link Layer | 
BT Baseband + RF | 

## Slide 37: Resource (instance)
Resource:
  "Resource" means a specific "resource instance".
Resource features: a resource is determined with the following features.
  URI
    In general, a resource can have any URI but some special resources have pre-defined URI.
  Property
    <Key: Value> pairs which characterize the resource.
  OCF Link
    establish a relationship among resources.
/resource1URI
Property 1 <key1: value1>
Property 2 <key2: value2>
Typed Web link
/resource2URI
Property 3 <key3: value3>
Property 4 <key4: value4>
link

## Slide 38: Resource (instance)
Resource:
  "Resource" means a specific "resource instance".
Resource features: a resource is determined with the following features.
  URI
    In general, a resource can have any URI but some special resources have pre-defined URI.
  Property
    <Key: Value> pairs which characterize the resource.
  OCF Link
    establish a relationship among resources.
/myLightSwitch
{
"n": MyRoomLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"]
"id": "b.switch_TF38_3",
"value": true
}

## Slide 39: Property
Property is “key-value” pair and specified with the following features
Property title: a human friendly name (e.g., interface)
Property name: the key in "key-value" pair, (e.g., if)
Value type: the type of value, integer, string, float (e.g., integer)
Value rules: the rule for the value, (e.g., minimum: 0)
Unit: the unit of the value, (e.g., celcius)
Mandatory: indicate whether the property is mandatory or optional in the corresponding resource, (e.g., mandatory)
Access mode: indicate the access mode for the property e.g.,) Read Only
Description: describes the property (e.g., indicates the current temperature)

## Slide 40: Property: Format
Format for property specification: Table
  Property is specified with the following table with 8 columns.
Property title | Property name | Value type | Value rule | Mandatory | Access mode | Unit | Description
Name | n | string | recommended that the length be restricted to 64 characters (UTF-8)) | Mandatory | Read Only |  | Human friendly name of a resource (e.g., “n”: “MyLivingRoomLight”)
Ex) Name (“n”) property specification
Quiz
What is the difference between “property name” & “name property”?
What is the name property name?
What is the name property title?

## Slide 41: Property: Common Property
Common property is the property which keeps its semantic meaning intact independent of the resources for which it’s attached.
  In general, property has a meaning only within the resource for which it is defined. Under a different resource, the same property name may mean the entirely different thing.
    For example, “value” property may mean boolean under binary switch resource but number under temperature resource.
  Some property called “Common property“ keeps its meaning intact across resources.
Property title | Property name | Value type | Value rule | Unit | Access mode | Mandatory | Description
Resource Type | rt | array | Array of strings, conveying Resource Type IDs to which the Resource belongs |  | R | Yes | The property name rt is as described in IETF RFC 6690
Interface | if | array | Array of strings, conveying Interfaces which the Resource support |  | R | Yes | Property to declare the Interfaces supported by a Resource.
Name | n | string |  |  | R, W | No | Human understandable name for the resource.
Resource Identity | id | string | Implementation Dependent |  | R | No | Unique identifier of the Resource (over all Resources in the Device)

## Slide 42: Resource Type
Resource Type is a class of resources and specified with the following features
Resource Type title: a human friendly name for the resource type. (e.g., humidity)
Resource Type ID: the string included in “rt” property value. (e.g., oic.r.humidity)
Resource interfaces: The interfaces that could be supported by the resource type.
Fixed URI (optional): for special resources with a priori fixed URI. (e.g., /oic/res)
Mandatory: indicate whether the Resource Type is mandatory or optional (e.g., mandatory)
Description: describe the Resource Type, (e.g., the resource describes the environment humidity.)
(related) Resource Types (optional): other Resource Types that may be referenced in this Resource Type, applicable to collections.
Properties: all the properties associated with this Resource Type.

## Slide 43: Resource Type: Format
Resource Type is a class or category of Resources & specified with
i) The table for Resource Type & ii) The table for associated properties
Ex) “Binary Switch” Resource Type Specification
Property title | Property name | Value type | Value rule | Unit | Access mode | Mandatory | Description
Name | n | string |  |  | R | No | Human friendly name For example, “My Light Switch”
Resource Type ID | rt | string |  |  | R | yes | Represent a specific resource type.
Interface | if | string |  |  | R | Yes | Unique identifier for device (UUID)
Value | value | Boolean |  |  | RW | yes | Status of the switch
Binary switch properties
fixed URI | Resource Type Title | Resource Type ID (“rt” value) | interfaces | Description | Related Functional Interaction | M/CM/O
none | Binary switch | oic.r.switch.binary | oic.if.a, oic.if.baseline | Binary switch to turn on-off the device to which it’s associated. | Actuation | O

## Slide 44: OCF Link: Typed Web Link
Type web link (RFC 5988) which is a means of expressing connections between resources.
Context URI: indicate the resource determining the relationship context. (e.g. /myRoom)
Target URI: indicate the resource determining the relationship target. (e.g. /myLight)
Relation: a relationship from the context URI to target URI. (e.g. "inside" )
Attributes: a set of attributes that provide metadata about the target URI. (e.g. “rt“)
{
"Context URI": /myRoom,
"Target URI": /myLgith,
"relationship": "inside",
"resource type for target URI": "oic.r.light"
}
(conceptual) example) of Typed Web link
from room to light

## Slide 45: OCF Link
OCF Link consist of Parameters which are key-value pairs characterize link relationship.
anchor: context URI, default value of hosting Resource when absent
href: target URI, mandatory
rel: relationship, the default value of “hosts” when absent
rt: Resource Type ID of the target Resource, mandatory
if: The Interfaces which the target Resource supports, mandatory
p: bitmap indicating discoverabiliy & observability of target resource
eps: Endpoints (i.e., IP address + port #) with which the target Resource can be accessed.
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rel": "hosts",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}

## Slide 46: Collection: Resource structure
Flat structure among Resources
  No hierarchy among Resources, no sub-Resource & Resource are organized with Link
Collection
  A Resource with OCF Links
    “links” Property with an array of OCF Links as its value.
{
"rt": ["oic.wk.col"],
"if": ["oic.if.ll", "oic.if.baseline", "oic.if.b"],
"links": [
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myFanSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:a::b1d4]:33333"}]
}
]
}

## Slide 47: Interface
(Tentatively) Defines interaction constraints on a Resource
  Which properties are exposed
  Which methods are allowed – retrieve-only or updateable
  How links are processed; oic.if.b
  Application semantics –
    for example oic.if.s and oic.if.a for sensors and actuators vs. oic.if.r and oic.if.rw for status and configuration parameters
Specifies several interfaces
  Further elaboration or clarification .
Interface 보충

## Slide 48: Query: “rt” & “if” query
“if” query specifies to indicate the “interface” to use
  POST /exampleCollectionURI?if=oic.if.b
“rt” query specified as a filter
{
"rt": ["oic.wk.col"],
"if": ["oic.if.ll", "oic.if.baseline", "oic.if.b"],
"links": [
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myFanSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:a::b1d4]:33333"}]
}
]
}
GET /collection
?rt=oic.r.switch.binary
RESPONSE
[ {
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}, ]
REQUEST
Query example 보충

## Slide 49: Core Resources
Core Resources
  ATG defines several Resource Types which are common to all verticals.
fixed URI | Resource Type Title | Resource Type ID (“rt” value) | interfaces | Description | Related Functional Interaction | M/CM/O
/oic/res | Default | oic.wk.res | oic.if.ll, oic.if.baseline | expose the Resources hosted by the responding Server and facilitate OCF Device discovery. | Discovery | M
/oic/d | Device | oic.wk.d | oic.if.r, oic.if.baseline | expose the Property of logical OCF Device (e.g., Device Type). | Discovery | M
/oic/p | Platform | oic.wk.d | oic.if.r, oic.if.baseline | expose the Property of physical platform. | Discovery | M

## Slide 50: Core Resources: Examples
{
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"di": "dc70373c-1e8d-4fb3-962e-017eaa863989",
"icv": "ocf.1.0.0",
"dmv": "ocf.res.1.0.0, ocf.sh.1.0.0",
"piid": "6F0AAC04-2BB0-468D-B57C-16570A26AE48"
}
{
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"links": [
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/res",
"rel": "self",
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:a::b1d4]:33333"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/d",
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/p",
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightBrightness",
"rt": ["oic.r.brightness"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}
]
}
{
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"pi": "54919CA5-4101-4AE4-595B-353C51AA983C",
"mnmn": "STRK, Inc"
}
/oic/res
/oic/d
/oic/p

## Slide 51: OCF Device
OIC device is specified
  with i) core resources & ii) device specific resources.
    Device type specified by “oic.d.<device type>”, (e.g., oic.d.light)
  For example “light device (oic.d.light)” shall have mandatory
    Core resource ① /oic/res, ② /oic/d, ③ /oic/p (with fixed URI),
    Device specific resource ③ binary switch (with free URI)
OIC device construct
/oic/res
/oic/d
/resource1URI
/resource2URI
oic/d (with “rt”=“oic.d.<device type>”
* oic core resource with fixed URI
Resource2
* Device specific resource with free URI
oic/res
* oic core resource with fixed URI
Resource1
* Device specific resource with free URI

## Slide 52: Device example: light device (oic.d.light)
/oic/res
[{
"di": "example_device_id",
"links": [
{ "href": "/oic/d",
"rt": "oic.d.light",
"if": "oic.if.r",
"rel": "hosts"},
{ "href": "/myLightSwitch",
"rt": "oic.r.switch.binary",
"if": "oic.if.a",
"rel": "hosts"},
{ "href": "/myLightBrigtness",
"rt": "oic.r.light.brightness",
"if": "oic.if.a",
"rel": "hosts"}
]
}]
/oic/d
{
"n": "myRoomLightDevice",
"rt": “oic.d.light",
"if": "oic.if.r",
“di": "example_device_id“,
"icv": "oic.1.5"
}
/myLightBrightness
{
"n": MyRoomLightBrightness",
"rt": "oic.r.light.brightness",
"if": "oic.if.a",
"id": “light_brightenss_TF38_3",
"value": 30
}
/myLightSwitch
{
"n": MyRoomLightSwitch",
"rt": "oic.r.switch.binary",
"if": "oic.if.a",
"id": "b.switch_TF38_3",
"value": "true"
}

## Slide 53: Discovery procedure with oic/res
GET /oic/res
RESPONSE
Device discovery with “oic/res”
  A response to “oic/res” carries device type in “rt” of “oic/d” in addition to all resource information.
[{
"di": "example_device_id",
"links": [
{"href": "/oic/d",
"rt": "oic.d.light",
"if": "oic.if.r",
"rel": "hosts"},
{ "href": "/myLightSwitch",
"rt": "oic.r.switch.binary",
"if": "oic.if.a",
"rel": "hosts"},
{ "href": "/myLightBrigtness",
"rt": "oic.r.light.brightness",
"if": "oic.if.a",
"rel": "hosts"}
]
}]
/oic/res
[{
"di": "example_device_id",
"links": [
{"href": "/oic/d",
"rt": "oic.d.light",
"if": "oic.if.r",
"rel": "hosts"},
{ "href": "/myLightSwitch",
"rt": "oic.r.switch.binary",
"if": "oic.if.a",
"rel": "hosts"},
{ "href": "/myLightBrigtness",
"rt": "oic.r.light.brightness",
"if": "oic.if.a",
"rel": "hosts"}
]
}]
/oic/d
{
"n": "myRoomLightDevice",
"rt": “oic.d.light",
"if": "oic.if.r",
“di": “example_device_id",
"icv": "oic.1.5"
}
/myLightSwitch
{
"n": MyRoomLightSwitch",
"rt": "oic.r.switch.binary",
"if": "oic.if.a",
"id": "b.switch_TF38_3",
"value": "true"
}
/myLightBrightness
{
"n": MyRoomLightBrightness",
"rt": "oic.r.light.brightness",
"if": "oic.if.a",
"id": “light_brightenss_TF38_3",
"value": 30
}

## Slide 54: CRUDN: generic operation procedure
CREATE
RETRIEVE
UPDATE
DELETE
NOTIFICATION
  Subscribed notification
    A client makes a priori subscription for a target resource of interest to the hosting server.
  Unsubscribed notification
    No a priori subscription for the target resource.
    Ex) Fire alarm or VANET emergency

## Slide 55: Generic communication flow scheme
Client
Server
Request
Response
CRUD & N operation

## Slide 56: Generic communication flow scheme
(tentative) Request message parameter/ Operation | 
Operation (op) | operation to be executed, i.e. CRUD&N(?)
Subscription indication (observe opt?) | Request to notify upon resource state change
To (to) | The identifier (URI) of the target resource for the operation
From (fr) | the identifier of the message Originator in URI (ex) Device ID, Client ID or APP ID
Request Identifier (ri) | uniquely identifies a Request message
Content (cn) | contents (resource representation) to be transferred
Request expiration Timestamp (ot) (?) | Till when the message is valid (?)
(tentative) Response message parameter/ Results | 
Operation (op) (?) | operation to be executed, i.e. N
Response Code (rs) | successful, unsuccessful, Unsolicited N (?)
To (to) | the identifier of the message Originator, ‘fr’ in the matching request or multicast address in case of unsubscribed notification
From (fr) | The identifier of the target resource, ‘to’ in the matching request or the identifier or message originator in case of unsubscribed notification.
Request Identifier (ri) | uniquely identifies a Request message (or a priori fixed value)
Content (cn) | contents (resource representation) to be transferred
Response Expiration Timestamp (ot)? | when the request message expires
Issue: Notification indication
For CoAP, notification is indicated with observe option & CoAP code.

## Slide 57: CRUDN & POST/PUT/GET/DELETE
No one-to-one correspondence between CRUDN & POST/PUT/GET/DELETE.
CREATE is performed with POST or PUT
UPDATE is performed with POST or PUT
CREATE with POST: i) Existing target URI for the resource responsible for creation & ii) the URI of the new resource is determined by the server, forwarded to the client.
CREATE with PUT: i) Non existing target URI for the new resource to be created.
UPDATE with POST: i) Existing target URI for the resource to be updated & ii) partial modification with the payload.
UPDATE with PUT: i) Existing target URI for the resource to be updated & ii) whole replacement with the payload.

## Slide 58: UPDATE with POST
UPDATE with POST: i) Existing target URI for the resource to be updated & ii) partial modification with the payload.
POST /existingURI
OIC server
{
“value": “False”
}
/existingURI
{
"n": MyRoomFoo",
"rt": "oic.r.foo",
"if": "oic.if.a",
“value": “True”
}

## Slide 59: UPDATE with POST
UPDATE with POST: i) Existing target URI for the resource to be updated & ii) partial modification with the payload.
POST /existingURI
OIC server
/existingURI
{
"n": MyRoomFoo",
"rt": "oic.r.foo",
"if": "oic.if.a",
“value": “False”
}
{
“value": “False”
}

## Slide 60: UPDATE with PUT
UPDATE with PUT: i) Existing target URI for the resource to be updated & ii) whole replacement with the payload.
PUT /existingURI
OIC server
/existingURI
{
"n": MyRoomFoo",
"rt": "oic.r.foo",
"if": "oic.if.a",
“value": “True”
}
{
“value": “False”
}

## Slide 61: UPDATE with PUT
UPDATE with PUT: i) Existing target URI for the resource to be updated & ii) whole replacement with the payload.
PUT /existingURI
OIC server
/existingURI
{
“value": “False”
}
{
“value": “False”
}

## Slide 62: Background: How to add a single ACE to an ACL
Cumbersome to Add/ Replace/ Remove an item of an array.
  requires to send all the array items in UPDATE payload (i.e. POST payload).
The issue is that if you want to add one item to an array, you have to RETRIEVE the value, add your item to the list and then UPDATE the entire array value including the old items and the one you intend to add. If the Property value happens to change between the RETRIEVE and the UPDATE operations, you’ll lose those changes.
Would be convenient to enable POST to Append/ Update/ Delete an item of an array.
  IETF Core WG is working on the issue with
  Patch and Fetch Methods for CoAP (https://tools.ietf.org/html/draft-ietf-core-etch-01)
  The above permits to access & manipulate parts of a resource with new methods FETCH & PATCH/iPATCH.

## Slide 63: PATCH
PATCH REQUEST contains "Patch document“ which instructs how the target resource (referred by Request URI) should be modified to produce a new version.
  op: the operation to perform (add, replace, remove, copy(?), move(?))
  path: the target to operate.
  value: the value to be incorporated
For the case of adding one item & replacing another to an existing array, it works like this.
[
{ "op":"replace","path":"foo/1","value":{"A":5}}
{ "op":"add","path":"bar/1","value":{"E":6}}
]

## Slide 64: PATCH example
Resource original state
REQ: PATCH /Resource
RET: CoAP 2.04 Changed
REQ: PATCH /Resource
{ "foo": [{"A":1}, {"B":2}], "bar": [{"C":3}, {"D":4}]}
[ { "op":"replace","path":"foo/1","value":{"A":5}}
{ "op":"add","path":"bar/1","value":{"E":6}} ]
{"foo": [{"A":5}, {"B":2}], "bar": [{"E":6}, {"C":3}, {"D":4}]}

## Slide 65: PATCH using POST with query
Resource original state
REQ: POST /Resource?op=add
RET: CoAP 2.04 Changed
REQ: POST /Resource
{ "foo": [{"A":1}, {"B":2}], "bar": [{"C":3}, {"D":4}]}
{"foo": [{"A":1}, {"B":2}], "bar": [{"E":6}, {"C":3}, {"D":4}]}
{ “bar/1": [{“E“:6}]}

## Slide 66: Next step
Assess the feasibility
  Would it be nice to adopt PATCH into OCF?
  Can we use query based approach also?

## Slide 67: Background
“rt” query is specified for /oic/res
  GET /oic/res?rt=oic.r.foo would return the OCF Links with “rt” Parameter value is “oic.r.foo”, (e.g. {“href”: “/resource”, “rt”: “oic.r.foo”, “if”: “oic.if.baseline”})
  In case of multiple matching Links, the response would carry the multiple Links.
However “rt” query is underspecified
  it’s not clear
    whether “rt” query applicable to all the Resource Types
    or only to Collections
    or only to /oic/res
  if “rt” query is not limited to /oic/res, it’s not clear
    “rt” query value matches with “rt” Link Parameter or
    “rt” Property.
Michael proposed an approach to differentiate “rt” query based on interface, which , IMO, is of use.
PATCH

## Slide 68: Michael’s “rt” query proposal as I understand it.
“rt” query behaves in a different way according to interface used.
  This is to present the proposal before deciding on its feasibility or desirability.
“oic.if.ll”: select the matching Link.
  if "rt" query is used with "oic.if.ll", i.e. GET ?rt=oic.r.foo&if=oic.if.ll,
  the Sever returns the Links with “rt” Parameter having the query value.
“oic.if.{a, s, r, rw, baseline}”: select the matching Property
  if "rt" query is used with "oic.if.{a, s, r, rw, baseline}", i.e. GET ?rt=oic.r.foo&if=oic.if.baseline
  the Server respond only when the query value is an item of “rt” Property Value of the target Resource & sends back only the Properties associated with the query value.
“oic.if.b”: selecting the matching Link to forward the Request.
  if "rt" query is used with "oic.if.b", i.e. GET ?rt=oic.r.foo&if=oic.if.b
  the Server forwards the Request only through the Links with “rt” Parameter having the query value.

## Slide 69: Examples: Target Collection
{ "rt": ["oic.wk.col"], "if": ["oic.if.ll","oic.if.baseline", "oic.if.b"], "links": [ { "href": "/BinarySwitchResURI", "rt": ["oic.r.switch.binary"], "if": ["oic.if.baseline","oic.if.a"], "p": {"bm": 1,"sec": false} },
{ "href": "/TemperatureResURI", "rt": ["oic.r.temperature"], "if": ["oic.if.baseline","oic.if.a"], "p": {"bm": 1,"sec": false} } ] }

## Slide 70: Example: oic.if.ll
GET /collection?rt=oic.r.switch.binary&if=oic.if.ll
{ "rt": ["oic.wk.col"], "if": ["oic.if.ll","oic.if.baseline", "oic.if.b"], "links": [ { "href": "/BinarySwitchResURI", "rt": ["oic.r.switch.binary"], "if": ["oic.if.baseline","oic.if.a"], "p": {"bm": 1,"sec": false} },
{ "href": "/TemperatureResURI", "rt": ["oic.r.temperature"], "if": ["oic.if.baseline","oic.if.a"], "p": {"bm": 1,"sec": false} } ] }

## Slide 71: Example: oic.if.ll
GET /collection?rt=oic.r.switch.binary&if=oic.if.ll
  The response is
[ { "href": "/BinarySwitchResURI", "rt": ["oic.r.switch.binary"], "if": ["oic.if.baseline","oic.if.a"], "p": {"bm": 1,"sec": false,"tcp": 57276} } ]

## Slide 72: Example: oic.if.{a, s, rw, r, baseline}
{ "rt": ["oic.wk.col"], "if": ["oic.if.ll","oic.if.baseline", "oic.if.b"], "links": [ { "href": "/BinarySwitchResURI", "rt": ["oic.r.switch.binary"], "if": ["oic.if.baseline","oic.if.a"], "p": {"bm": 1,"sec": false} },
{ "href": "/TemperatureResURI", "rt": ["oic.r.temperature"], "if": ["oic.if.baseline","oic.if.a"], "p": {"bm": 1,"sec": false} } ] }
GET /collection?rt=oic.r.switch.binary&if=oic.if.baseline
  silent discard or error response
No Match

## Slide 73: Example: oic.if.{a, s, rw, r, baseline}
GET /collection?rt=oic.wk.col&if=oic.if.baseline
{ "rt": ["oic.wk.col"], "if": ["oic.if.ll","oic.if.baseline", "oic.if.b"], "links": [ { "href": "/BinarySwitchResURI", "rt": ["oic.r.switch.binary"], "if": ["oic.if.baseline","oic.if.a"], "p": {"bm": 1,"sec": false} },
{ "href": "/TemperatureResURI", "rt": ["oic.r.temperature"], "if": ["oic.if.baseline","oic.if.a"], "p": {"bm": 1,"sec": false} } ] }

## Slide 74: Example: oic.if.{a, s, rw, r, baseline}
GET /collection?rt=oic.wk.col&if=oic.if.baseline
  The response is
{ "rt": ["oic.wk.col"], "if": ["oic.if.ll","oic.if.baseline", "oic.if.b"], "links": [ { "href": "/BinarySwitchResURI", "rt": ["oic.r.switch.binary"], "if": ["oic.if.baseline","oic.if.a"], "p": {"bm": 1,"sec": false} },
{ "href": "/TemperatureResURI", "rt": ["oic.r.temperature"], "if": ["oic.if.baseline","oic.if.a"], "p": {"bm": 1,"sec": false} } ] }

## Slide 75: Example: oic.if.b
GET /collection?rt=oic.r.switch.binary&if=oic.if.b
  Forward the Request only to the matching Links, i.e. /BinarySwitchResURI
{ "rt": ["oic.wk.col"], "if": ["oic.if.ll","oic.if.baseline", "oic.if.b"], "links": [ { "href": "/BinarySwitchResURI", "rt": ["oic.r.switch.binary"], "if": ["oic.if.baseline","oic.if.a"], "p": {"bm": 1,"sec": false} },
{ "href": "/TemperatureResURI", "rt": ["oic.r.temperature"], "if": ["oic.if.baseline","oic.if.a"], "p": {"bm": 1,"sec": false} } ] }

## Slide 76: Example: oic.if.b
[ { "href": "/BinarySwitchResURI", "rep": {"value": true} } ]
GET /collection?rt=oic.r.switch.binary&if=oic.if.baseline
  The response is

## Slide 77: Next step
Assess the feasibility or desirability of the approach
Which “rt” query is to be specified?
  “rt” query for /oic/res?
  “rt” query for Collection?
  “rt” query for multi-value “rt” Resource?
    This is the request from BTG

## Slide 78: (tentative) Proposal
Specify “rt” query for the following
  “rt” query for /oic/res
    GET /oic/res?rt=oic.r.foo (with “oic.if.ll”)
  “rt” query for Collection
    GET /collection?rt=oic.r.foo (with “oic.if.ll”)
    GET /colleciton?rt=oic.r.foo&if=oic.if.b (with “oic.if.b”)
    POST /colleciton?rt=oic.r.foo&if=oic.if.b (with “oic.if.b”)
  “rt” query for multi-value “rt”
    We need a joint talk with BTG.
The above is requested from developers with use cases.

## Slide 79: appendix
“rt” query for multi-value “rt” Resource

## Slide 80: One more thing: “rt” query from multi-value “rt” Resource
{ "rt": ["oic.r.switch.binary“, “oic.r.temperature”], "if": ["oic.if.a","oic.if.baseline”], "value": true,
"temperature": 22,
"range": [0,100],
"units": "C” }
“rt” query from multi-value “rt” Resource
  Returns only the Properties belonging to the matching Resource Type.
  This is only to facilitate mutual understanding.
Example: Resource with “oic.r.switch.binary” & “oic.r.temperature”

## Slide 81: One more thing: “rt” query from multi-value “rt” Resource
{ "rt": ["oic.r.switch.binary“, “oic.r.temperature”], "if": ["oic.if.a","oic.if.baseline”], "value": true,
"temperature": 22,
"range": [0,100],
"units": "C” }
“rt” query from multi-value “rt” Resource
  Returns only the Properties belonging to the matching Resource Type.
  This is only to facilitate mutual understanding.
Example: Resource with “oic.r.switch.binary” & “oic.r.temperature”
  GET /Resource?rt=oic.r.switch.binary

## Slide 82: One more thing: “rt” query from multi-value “rt” Resource
{ "value": true
}
“rt” query from multi-value “rt” Resource
  Returns only the Properties belonging to the matching Resource Type.
  This is only to facilitate mutual understanding.
Example: Resource with “oic.r.switch.binary” & “oic.r.temperature”
  GET /Resource?rt=oic.r.switch.binary
    Would return only the Properties belonging to “oic.r.switch.binary”

## Slide 83: Discovery
Direct vs Indirect discovery
  Direct communication between discovering & discovered devices.
  3rd party assisted discovery
Pull vs Push based discovery
  Pull
  Push
Current OCF discovery
  CoAP discovery: direct & pull based
  Resource Directory: indirect & pull based

## Slide 84: Discovery procedure with oic/res
GET /oic/res
RESPONSE
Device discovery with “oic/res”
  A response to “oic/res” carries device type in “rt” of “oic/d” in addition to all resource information.
[{
"di": "example_device_id",
"links": [
{"href": "/oic/d",
"rt": "oic.d.light",
"if": "oic.if.r",
"rel": "hosts"},
{ "href": "/myLightSwitch",
"rt": "oic.r.switch.binary",
"if": "oic.if.a",
"rel": "hosts"},
{ "href": "/myLightBrigtness",
"rt": "oic.r.light.brightness",
"if": "oic.if.a",
"rel": "hosts"}
]
}]
/oic/res
[{
"di": "example_device_id",
"links": [
{"href": "/oic/d",
"rt": "oic.d.light",
"if": "oic.if.r",
"rel": "hosts"},
{ "href": "/myLightSwitch",
"rt": "oic.r.switch.binary",
"if": "oic.if.a",
"rel": "hosts"},
{ "href": "/myLightBrigtness",
"rt": "oic.r.light.brightness",
"if": "oic.if.a",
"rel": "hosts"}
]
}]
/oic/d
{
"n": "myRoomLightDevice",
"rt": “oic.d.light",
"if": "oic.if.r",
“di": “example_device_id",
"icv": "oic.1.5"
}
/myLightSwitch
{
"n": MyRoomLightSwitch",
"rt": "oic.r.switch.binary",
"if": "oic.if.a",
"id": "b.switch_TF38_3",
"value": "true"
}
/myLightBrightness
{
"n": MyRoomLightBrightness",
"rt": "oic.r.light.brightness",
"if": "oic.if.a",
"id": “light_brightenss_TF38_3",
"value": 30
}

## Slide 85: Current status & aim
Resource directory (RD) is needed for Cloud operation and OSWG/IoTivity is implementing the feature with product plan.
However RD is underspecified and its contents scattered in the spec document & RAML/JSON files, which may cause Spec & code divergence with dire consequence.
CR78 (bug# 1060) is submitted to complement the current RD spec to achieve spec & code alignment.
  CR78 took into consideration not only the existing specification but also IoTivity implementation.

## Slide 86: CR 78 contents: 3 RD features
RD definition
  An OCF Device facilitating indirect discovery by exposing 3rd party Resources (i.e. Links) with mandatory “oic.wk.rd” Resource Type.
RD features
  RD discovery
    Discover an RD and select one.
    Relies on “oic.wk.rd” without proper definition
  Resource publish
    publish/update/delete Resource (i.e. Links) in /oic/res of an RD
    Under specified, also relies on “oic.wk.rd” & “oic.w,.rdpub”
  Resource exposure
    Expose published Resources via /oic/res of RD
    Mature via multiple discussions during “Endpoint/ Bridging” specification.

## Slide 87: CR 78 contents: main works
"oic.wk.rd" Resource Type specification
  provides selection criteria with GET /oic/rd
  allow Resource publish/update with POST /oic/rd
  allow Resource delete with DELETE /oic/rd
  incorporating "oic.wk.rdpub" into "oic.wk.rd“
Resource publish/update/delete elaboration
  initial publish of a new Link with POST /oic/rd (without “ins”)
  subsequent update of an existing Link with POST /oic/rd (with “ins”)
  delete of Link(s) with DELETE /oic/rd (with "di" or "ins" query)
RAML/JSON update
  rdpub.raml, oic.rd.selection-schema (for GET response), oic.rd.publish-schema (POST request & response and DELETE request & response).

## Slide 88: “oic.wk.rd” specification
“oic.wk.rd” Resource Type Specification
“oic.wk.rd” Properties
Property title | Property name | Value type | Value rule | Unit | Access mode | Mandatory | Description
Selector | sel | Integer or JSON Object |  |  | R | Yes | Provides the criteria for RD selection. Either JSON Object describing the selection criteria (e.g. Power) specified in 11.3.6.2.2.1 or an integer representing a bias factor calculated by RD. The value is in the range of 0 to 100 - 0 implies that RD is not to be selected. Client chooses RD with highest bias factor or randomly between RDs that have same bias factor.
fixed URI | Resource Type Title | Resource Type ID (“rt” value) | interfaces | Description | Related Functional Interaction | M/CM/O
/oic/rd | Resource Directory | oic.wk.rd | oic.if.baseline | The discoverable Resource Type through with which an RD 1) facilitates its discovery and provides the criteria to select an RD and 2) allows OCF Devices to publish, update and delete their Links in /oic/res of the RD. An OCF Device can find the presence of oic.wk.rd to discover an RD, then sends GET request to /oic/rd to acquire the selection criteria. An OCF Device can send POST request with Links in its payload to expose those Links in /oic/res of the RD. Also OCF Device can send DELTE request with suitable query (e.g. “di” or “ins”) to remove its Links from /oic/res of the RD. | Discovery | CM for RD

## Slide 89: RD discovery
GET /oic/res?rt=oic.wk.rd
Resource Directory
/oic/res
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]}
]
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
/oic/res response

## Slide 90: RD select
GET /oic/rd
Resource Directory
/oic/res
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]}
]
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
/oic/rd response
{
"rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"],
"sel": 50
}

## Slide 91: Resource publish
POST /oic/rd
Resource Directory
/oic/res
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]}
]
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
{
"di": "88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49 ",
"links": [
{
"anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [
{"ep": "coaps://[fe80::b1d6]:22222"}]},
"ttl": 600
}

## Slide 92: Resource publish
POST /oic/rd
Resource Directory
/oic/res
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch", "rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d6]:22222"}],
"ins": 11235 }
]
POST response
{
"di": "88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"links": [
{
"anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [
{"ep": "coaps://[fe80::b1d6]:22222"}],
"ins": 11235},
"ttl": 600
}

## Slide 93: Resource update
POST /oic/rd
Resource Directory
/oic/res
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
{
"di": "88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49 ",
"links": [
{
"anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [
{"ep": "coaps://[fe80::b1d6]:1111"}],
"ins": 11235},
"ttl": 600
}
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch", "rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d6]:22222"}],
"ins": 11235 }
]

## Slide 94: Resource update
POST /oic/rd
Resource Directory
/oic/res
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch", "rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d6]:1111"}],
"ins": 11235 }
]
POST response
{
"di": " 88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"links": [
{
"anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [
{"ep": "coaps://[fe80::b1d6]:1111"}],
"ins": 11235},
"ttl": 600
}

## Slide 95: Resource delete
DELETE?ins=11235
Resource Directory
/oic/res
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch", "rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d6]:1111"}],
"ins": 11235 }
]

## Slide 96: Resource delete
DELETE?ins=11235
Resource Directory
/oic/res
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]}
]

## Slide 97: Resource delete
DELETE?ins=11235
Resource Directory
/oic/res
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]}
]
DELETE response: success

## Slide 98: Issues
Single RD selection
  Currently a publishing Device SHALL select/publish only one RD.
  There is no interoperability issue to select multiple RDs, especially when each RD resides in different domain (one in States, one in Korea).
  Changed to “SHOULD”
No response after publishing
  Currently a publishing Device SHALL NOT response for a published Resource
  there is no interoperability issue when a publishing Device replies, only performance inefficiency.
  Changed to “SHOULD”

## Slide 99: PATCH

## Slide 100: Content Negotiation

## Slide 101: Bridging

## Slide 102: Further works?
More minute Resource manipulation
  Part of Resource RETRIVE or UPDATE
    Long array update
    PATCH would be of help
  Group management
    Dim down the light, Close the Window & Play the movie
    Group/Scene/Script/Rule
  Time dependent operation with delay or reservation(?)
    Turn off the light 10 min later
    Action & Actuation Resource(?)
    Form may help?
Standardized IETF/IRTF/WoT specification would be of help

## Slide 103: Appendix

## Slide 104: Main IoT Technical Challenges vs Internet
Networked Embedded Device
Big Data Analysis
IoT Network
UX
IoT Core Framework
IoT Standard
IoT Security 기술
Sensor
Sensor
Service Server
Gateway
Actuator
Actuator
Connectivity
User
Device
Web server
LAN, WLAN
TCP/ IP
WWW
Search (?)
IPSec, DES
Web Browser
IETF & W3C & IEEE & 3GPP

## Slide 105: Main IoT Technical Challenges vs Internet
Networked Embedded Device
Big Data Analysis
IoT Network
UX
IoT Core Framework
IoT Standard
IoT Security 기술
Sensor
Sensor
Service Server
Gateway
Actuator
Actuator
Connectivity
User
Device
Web server
LAN, WLAN
TCP/ IP
WWW
Search (?)
IPSec, DES
Web Browser
IETF & W3C & IEEE & 3GPP
SUN
3Com
Cisco
NETSCAPE
Google
RSA
Apple

## Slide 106: (Example) NEST Operations with Protocols
NEST Thermostat
(Sensor & Actuator)
NEST
Service Server
Gateway
Monitoring with NEST thermostat (by Smartphone)
Smart Phone

## Slide 107: (Example) NEST Operations with Protocols
Smart Phone
NEST Thermostat
(Sensor & Actuator)
NEST
Service Server
Gateway
Monitoring with NEST thermostat (by Smartphone)
0. Event occurrence
1. Request NEST for temperature
1.1. data format with JSON
1.2. message & method with HTTP GET
1.3. delivery with TCP/IP
1.4. over the air with WiFi

## Slide 108: (Example) NEST Operations with Protocols
Smart Phone
NEST Thermostat
(Sensor & Actuator)
NEST
Service Server
Gateway
0. Event occurrence
1. Request NEST for temperature
1.1. data format with JSON
1.2. message & method with HTTP GET
1.3. delivery with TCP/IP
2. Response with temperature
1.4. over the air with WiFi
Monitoring with NEST thermostat (by Smartphone)
Simplified & further procedures needed
service discovery & ID resolution
lightweight network protocol
access control & security
et cetra…

## Slide 109: (Example) NEST Operations with Protocols
Smart Phone
NEST Thermostat
(Sensor & Actuator)
Gateway
Controlling with NEST thermostat (by NEST Service Server)
0. Event occurrence
NEST
Service Server

## Slide 110: (Example) NEST Operations with Protocols
Smart Phone
NEST Thermostat
(Sensor & Actuator)
NEST
Service Server
Gateway
Controlling with NEST thermostat (by NEST Service Server)
0. Event occurrence
1. Request NEST for temperature change
1.1. data format with JSON
1.2. message & method with HTTP PUT
1.3. delivery with TCP/IP
2. Change temperature with HVAC
1.4. over the air with WiFi

## Slide 111: (Example) NEST Operations with Protocols
Smart Phone
NEST Thermostat
(Sensor & Actuator)
NEST
Service Server
Gateway
Controlling with NEST thermostat (by NEST Service Server)
0. Event occurrence
1. Request NEST for temperature change
1.1. data format with JSON
1.2. message & method with HTTP PUT
1.3. delivery with TCP/IP
2. Change temperature with HVAC
1.4. over the air with WiFi
3. Response with state info
Simplified & further procedures needed
service discovery & ID resolution
lightweight network protocol
access control & security
et cetra…

## Slide 112: OCF Framework: IoT Platform
Transport
Networking
L2 Connectivity
Application profiles
Connected Health
Smart Home
Automotive
Retail
OCF Framework
ID & Addressing
Resource model
CRUDN
Messaging
Discovery
Device management
Security
Group management
Bridging
Streaming(?)
Cloud support (?)