## Slide 1: OCF 1.0 features: Endpoint
April 18, 2017
JinHyeock Choi

## Slide 2: Anti-trust Confidentiality Reminder
This is a reminder that all Open Connectivity Foundation (“OCF”) activities are subject to compliance with the Antitrust Compliance Policy for Open Connectivity Foundation (the “Policy”). Each individual participant and attendee at this meeting is responsible for complying with the Policy. Copies of the Policy are available within the Workgroup portal, or if applicable, may be immediately emailed to anyone in this meeting.
Additionally, this is a reminder that all discussions and disclosures at this meeting are subject to the Confidentiality provisions of the OIC’s Bylaws.

## Slide 3: Contents
Endpoint definition
Endpoint information with 2 items (ep, pri)
  ep has a URI value consisting of Transport Protocol Suites & Endpoint Locator
“eps” Parameter for Endpoint information
  /oic/res with “eps” Parameter
Endpoint discovery or retrieval

## Slide 4: Endpoint definition
RFC 7252 specified "Endpoint" as below
A CoAP endpoint is the source or destination of a CoAP message. The
specific definition of an endpoint depends on the transport being
used for CoAP. For the transports defined in this specification, the
endpoint is identified depending on the security mode used (see
Section 9): With no security, the endpoint is solely identified by an
IP address and a UDP port number. With other security modes, the
endpoint is identified as defined by the security mode.
Similarly OIC Endpoint is specified as
An (OCF) Endpoint is defined as the source or destination of a request and response messages for a given Transport Protocol Suites (e.g. CoAP over UDP over IPv6). The specific definition of an Endpoint depends on the Transport Protocol Suites being used. For the example of CoAP over UDP over IPv6, the endpoint is identified by an IPv6 address and UDP port number.

## Slide 5: Endpoint & OCF Device relationship
Each OCF Device shall associate with at least one Endpoint with which it can exchange Request & Response messages.
  When a message is sent to an Endpoint, it shall be delivered to the OCF Device which is associated with the Endpoint.
  When a Request message is delivered to an Endpoint, path component is enough to locate the target Resource.
OCF Device can be associated with multiple Endpoints.
  E.g. OCF Device may support both CoAP & HTTP
An endpoint can be shared among multiple OCF Devices, only when there is a way to clearly indicate the target Resource with Request URI.
  When multiple CoAP servers use separate URI paths for all the hosted resources, and the CoAP implementation demuxes by path, they can share the same CoAP endpoint.
  However, the above is not possible for OIC 1.1 because pre-determined URI (e.g. /oic/d) is mandatory for some mandatory Resources (e.g. "oic.wk.d")

## Slide 6: Endpoint information (i.e. Endpoint representation format)
Endpoint is represented by Endpoint information which consists of 2 items.
Endpoint (ep)
  ep in turn indicates Transport Protocol Suite & Endpoint Locator
Priority (pri)

## Slide 7: Endpoint (ep) : Transport Protocol Suites
Transport Protocol Suites
  Transport Protocol Suites is a combination of protocols (e.g. CoAP + UDP + IPv6)
  with which Request and Request message can be exchanged
  for RESTful transaction (i.e. CRUDN).
  Transport Protocol Suites is indicated by IANA registered “scheme”
  Vendor or OCF defined scheme is also allowed.
    example) com.samsung.foo
Transport Protocol Suites | scheme
coap + udp + ip | coap
coaps + udp + ip | coaps
coap + tcp + ip | coap+tcp
coaps+tco+ip | coaps+tcp
http + tcp + ip | http
https + tcp + ip | https

## Slide 8: Endpoint (ep): Endpoint Locator
Endpoint Locator (EPL)
  Endpoint Locator for is an address
  (e.g. IPv6 address + Port number) through which a message can be sent
  to the OCF Device
  (which is associated with the Endpoint).
  Endpoint Locator for “coap”, “coaps”, “coap+tcp”, “coaps+tcp”, “http”, “https” is represented as “IP address: port number”
    Example)
  [fe80::a4ca:5493:e96:3cea]:1111"

## Slide 9: Endpoint (ep) format
Endpoint (ep)
  “ep” is represented with URI (as specified in RFC3986)
  where “scheme” component indicates Transport Protocol Suites &
  “authority” does Endpoint Locator
  Example)
  "ep": "coap://[fe80::a4ca:5493:e96:3cea]:1111"
Transport Protocol Suites
Endpoint Locator

## Slide 10: “ep” value for Transport Protocol Suites
The current list of “ep” with corresponding Transport Protocol Suites is as below
Transport Protocol Suites | scheme | Endpoint Locator | "ep" Value example
coap + udp + ip | coap | IP address + port number | coap://[fe80::b1d6]:1111
coaps + udp + ip | coaps | IP address + port number | coaps://[fe80::b1d6]:1122
coap + tcp + ip | coap+tcp | IP address + port number | coap+tcp://[2001:db8:a::123]:2222
coaps + tcp + ip | coaps+tcp | IP address + port number | coaps+tcp://[2001:db8:a::123]:2233
http + tcp + ip | http | IP address + port number | http://[2001:db8:a::123]:1111
https + tcp + ip | https | IP address + port number | https://[2001:db8:a::123]:1122

## Slide 11: Priority (pri)
Priority (pri)
  When there are multiple “ep”, Priority “pri” indicated the priority or preference among them.
  “pri” is represented by a positive integer value & the lower the value, the higher the priority.
  Example
  "pri": 1
  “pri” is optional and may be omitted. The default “pri” value is 1, i.e. the absence of “pri” is equivalent to “pri”: 1.

## Slide 12: Endpoint information in “eps” Parameter
a new Link Parameter "eps" for Endpoint Information
  "eps" has an array of items as its value and each item represents Endpoint information with two key-value pairs, "ep" and "pri", of which "ep" is mandatory and "pri" is optional.
  "anchor" represents the hosting OCF Device, "href", target Resource and "eps" the two Endpoints for the target Resource.
  If the target Resource of a Link requires a secure connection (e.g. CoAPS), "eps" Parameter shall be used to indicate the necessary information (e.g. port number)
{
"anchor": "ocf://light_device_id",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coap://[fe80::b1d6]:1111", "pri": 2}, {"ep": "coaps://[fe80::b1d6]:1122"}]
}

## Slide 13: Endpoint discovery
We may define "Endpoint discovery" as the process for a Client to acquire the Endpoint information for OCF Device or Resource.
Implicit discovery
  If a Device is a source of a CoAP/ HTTP message (e.g. /oic/res response), the source IP address & port number can be combined to form the Endpoint Locator for the Device. Along with suitable “scheme” derived from the message & default “pri” value, Endpoint Information for the Device can be constructed.
Explicit discovery
  Endpoint information can be explicitly indicated with the "eps" Parameter of the Links in /oic/res.

## Slide 14: Endpoint information in /oic/res with “eps” Parameter
Endpoint for
each target resource.
[
{ "href": "/oic/res",
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989/oic/res",
"rel": "self",
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d6]:44444"}] },
{ "href": "/oic/p",
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989,
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coap://[fe80::b1d6]:44444"}, {"ep": "coaps://[fe80::b1d6]:11111"} ] },
{ "href": "/oic/d",
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989,
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coap://[fe80::b1d6]:44444"}, {"ep": "coaps://[fe80::b1d6]:11111"} ] },
{ "href": "/myLight",
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989,
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coap://[fe80::b1d6]:44444"}, {"ep": "coaps://[fe80::b1d6]:11111"} ] } ]
/oic/res

## Slide 15: CoAP based Endpoint discovery
CoAP multicast can be used for Endpoint discovery
Step1: CoAP Client sends a multicast GET to /oic/res.
Step2: CoAP Servers send back with unicast responses.
Step3: Upon receiving the response, the CoAP Client can use the source IP address & port number to form Endpoint information, when the /oic/res response doesn’t carry no explicit “eps” Value.
Step4: the CoAP Client can find out Endpoint information for the Resources from the “eps” Parameter in the Links targeting them.

## Slide 16: Appendix
Previous materials