## Slide 1: IoT a viewpoint from OIC experience
JinHyeock Choi
jinchoe@samsung.com

## Slide 2: contents
Overview
Main technical challenges
OIC architecture
  OIC functional block diagram
  OIC framework
OIC resource model
  Resource, URI, Link
  Property, Resource Type, OIC Device

## Slide 3
Overview

## Slide 4: Internet of Things ?
Cyper Physical System
Real World Internet
Ubiquitous Computing
M2M
Web of Thing
Internet of Everything

## Slide 5: Internet
Cyber World
User
Human
Cyber World open to Human
Digital

## Slide 6: Internet of Things (IoT)
User
Physical World
Human
Cyber World
Cyber & Physical World integrated & open to Human
Cyber World open to Human
Digital
Physical

## Slide 7
Challenges

## Slide 8: RESTful Architecture Style
Client
Server
RESTful Architecture (Representational State Transfer)
  Resource based operation
    Real world ‘entity’ is represented as ‘Resource’
  Resource manipulation via Request/ Response: CRUDN
Request
Response
CRUD & N operation
Resource (representation)
Resource (representation)
Addressable resources
A uniform, constrained interface
Representation based manipulation
Communicate statelessly
Hypermedia State Engine
REST Architecture Style
{
"n": "myRoomTemperature",
"rt": "oic.r.temperature",
"if": "oic.if.a",
"id": "example_id_xyz",
"temperature": 23,
"units": "C",
"setValue": 25
}
Physical entity
Entity handler

## Slide 9: (conceptual) IoT Architecture & Procedures
User
Device
Sensor
Sensor
Actuator
Gateway
Service Server
Actuator

## Slide 10: (conceptual) IoT Architecture & Procedures
User
Device
Sensor
Sensor
Actuator
Service Server
Actuator
Monitoring with sensors
0. Event occurrence
1. Request sensor for data
2. Response with data
Gateway

## Slide 11: (conceptual) IoT Architecture & Procedures
User
Device
Sensor
Sensor
Actuator
Service Server
Actuator
Monitoring with sensors
0. Event occurrence
1. Request sensor for data
2. Response with data
3. Notify without Request
Gateway

## Slide 12: (conceptual) IoT Architecture & Procedures
User
Device
Sensor
Sensor
Actuator
Service Server
Actuator
Controlling with actuators
0. Event occurrence
1. Request actuators for state transfer
2. Actuator action
3. Response with state information
Gateway

## Slide 13: (Example) NEST Operations with Protocols
NEST Thermostat
(Sensor & Actuator)
NEST
Service Server
Gateway
Monitoring with NEST thermostat (by Smartphone)
Smart Phone

## Slide 14: (Example) NEST Operations with Protocols
Smart Phone
NEST Thermostat
(Sensor & Actuator)
NEST
Service Server
Gateway
Monitoring with NEST thermostat (by Smartphone)
0. Event occurrence
1. Request NEST for temperature
1.1. data format with JSON
1.2. message & method with HTTP GET
1.3. delivery with TCP/IP
1.4. over the air with WiFi

## Slide 15: (Example) NEST Operations with Protocols
Smart Phone
NEST Thermostat
(Sensor & Actuator)
NEST
Service Server
Gateway
0. Event occurrence
1. Request NEST for temperature
1.1. data format with JSON
1.2. message & method with HTTP GET
1.3. delivery with TCP/IP
2. Response with temperature
1.4. over the air with WiFi
Monitoring with NEST thermostat (by Smartphone)
Simplified & further procedures needed
service discovery & ID resolution
lightweight network protocol
access control & security
et cetra…

## Slide 16: (Example) NEST Operations with Protocols
Smart Phone
NEST Thermostat
(Sensor & Actuator)
Gateway
Controlling with NEST thermostat (by NEST Service Server)
0. Event occurrence
NEST
Service Server

## Slide 17: (Example) NEST Operations with Protocols
Smart Phone
NEST Thermostat
(Sensor & Actuator)
NEST
Service Server
Gateway
Controlling with NEST thermostat (by NEST Service Server)
0. Event occurrence
1. Request NEST for temperature change
1.1. data format with JSON
1.2. message & method with HTTP PUT
1.3. delivery with TCP/IP
2. Change temperature with HVAC
1.4. over the air with WiFi

## Slide 18: (Example) NEST Operations with Protocols
Smart Phone
NEST Thermostat
(Sensor & Actuator)
NEST
Service Server
Gateway
Controlling with NEST thermostat (by NEST Service Server)
0. Event occurrence
1. Request NEST for temperature change
1.1. data format with JSON
1.2. message & method with HTTP PUT
1.3. delivery with TCP/IP
2. Change temperature with HVAC
1.4. over the air with WiFi
3. Response with state info
Simplified & further procedures needed
service discovery & ID resolution
lightweight network protocol
access control & security
et cetra…

## Slide 19: (conceptual) IoT Architecture & Procedures
User
Device
Sensor
Sensor
Actuator
Service Server
Actuator
Controlling & Monitoring
with sensor & actuator
Gateway

## Slide 20: Main IoT Technologies
User
Device
Sensor
Sensor
Actuator
Service Server
Actuator
Gateway

## Slide 21: Main IoT Technical Challenges
Networked Embedded Device
Sensor
Sensor
Service Server
Gateway
Actuator
Actuator
User
Device

## Slide 22: Main IoT Technical Challenges
Networked Embedded Device
Sensor
Sensor
Service Server
Gateway
Actuator
Actuator
Connectivity
User
Device

## Slide 23: Main IoT Technical Challenges
Networked Embedded Device
IoT Network
Sensor
Sensor
Service Server
Gateway
Actuator
Actuator
Connectivity 기술
User
Device

## Slide 24: Main IoT Technical Challenges
Networked Embedded Device
IoT Network
IoT Core Framework
Sensor
Sensor
Service Server
Gateway
Actuator
Actuator
Connectivity
User
Device

## Slide 25: Main IoT Technical Challenges
Networked Embedded Device
Big Data Analysis
IoT Network
IoT Core Framework
Sensor
Sensor
Service Server
Gateway
Actuator
Actuator
Connectivity
User
Device

## Slide 26: Main IoT Technical Challenges
Networked Embedded Device
Big Data Analysis
IoT Network
UX
IoT Core Framework
Sensor
Sensor
Service Server
Gateway
Actuator
Actuator
Connectivity
User
Device

## Slide 27: Main IoT Technical Challenges
Networked Embedded Device
Big Data Analysis
IoT Network
UX
IoT Core Framework
IoT Standard
IoT Security
Sensor
Sensor
Service Server
Gateway
Actuator
Actuator
Connectivity
User
Device

## Slide 28: Main IoT Technical Challenges vs Internet
Networked Embedded Device
Big Data Analysis
IoT Network
UX
IoT Core Framework
IoT Standard
IoT Security 기술
Sensor
Sensor
Service Server
Gateway
Actuator
Actuator
Connectivity
User
Device
Web server
LAN, WLAN
TCP/ IP
WWW
Search (?)
IPSec, DES
Web Browser
IETF & W3C & IEEE & 3GPP

## Slide 29: Main IoT Technical Challenges vs Internet
Networked Embedded Device
Big Data Analysis
IoT Network
UX
IoT Core Framework
IoT Standard
IoT Security 기술
Sensor
Sensor
Service Server
Gateway
Actuator
Actuator
Connectivity
User
Device
Web server
LAN, WLAN
TCP/ IP
WWW
Search (?)
IPSec, DES
Web Browser
IETF & W3C & IEEE & 3GPP
SUN
3Com
Cisco
NETSCAPE
Google
RSA
Apple

## Slide 30
OIC architecture

## Slide 31: RESTful Architecture Style
Client
Server
RESTful Architecture (Representational State Transfer)
  Resource based operation
    Real world ‘entity’ is represented as ‘Resource’
  Resource manipulation via Request/ Response: CRUDN
Request
Response
CRUD & N operation
Resource (representation)
Resource (representation)
Addressable resources
A uniform, constrained interface
Representation based manipulation
Communicate statelessly
Hypermedia State Engine
REST Architecture Style
{
"n": "myRoomTemperature",
"rt": "oic.r.temperature",
"if": "oic.if.a",
"id": "example_id_xyz",
"temperature": 23,
"units": "C",
"setValue": 25
}
Physical entity
Entity handler

## Slide 32: Logical organization: 3 part approach
Resource Type
Entity Handler
Entity (e.g. HW Sensor)
Resource
Resource
/s/hm/data
Relative URI
/192.168.1.1/s/hm/mgmt
Fully-qualified URI
Binding
Resource Address
OIC Server
OIC Client
CoAP
Device:
“Wrist Band”
Request
Response
Resolution: I
Range: I
Name: S
Time: UT
Rate: F
Name: S
Time: 11:30
Rate: 80
Name: Ravi HR
Representation
URI: /s/hm/data
GET
Protocol
Servlet
Resource Interface
RESTful transaction
Resource Model
Abstraction
[OIC Concepts & Architecture Review, Ravi Subramaniam]
Communication and Interoperability
(Protocol processing
& Messaging)
Resource model and organization
(Declarative)
Device abstraction (entity handler)
(Imperative)
RESTful transaction
Abstraction
Resource model

## Slide 33: IoT Protocol Stacks
DMC R&D Center ⓒ 2013 SAMSUNG Electronics Co.
6loWPAN
IPv6
6tisch
6lo
RFC 4862
RFC 4861
16ng
RFC 6459
ETSI TS102859
IEEE 802.3 Ethernet
IEEE 802.11 WiFi
IEEE 802.15.1 Bluetooth
IEEE 802.15.7 VLC
IEEE 802.15.4 Zigbee
IEEE 1901.2 PLC
IEEE 802.11 p C2C-CC
IEEE 802.16 WiMAX
Cellular 3GPP LTE
IP over Foo (PLC, VLC)
Geo-Networking
Energy Efficient Protocol
Delay Tolerant Transport
RPL
6light
homenet
eman
Ad-hoc VANET
Proxy/ Gateway
MIB
TCP
UDP
MPTCP
SCTP
RTP
ICMP
Access Control
AAA
EAP
DIAMETER
SSL/TLS
HTTP/ HTTPS
CoAP
MQTT
XMPP
DDS
DNS
Resource Abstract
URI/ ID
Meta data /Link
Resource Representation
Attributes
Structure/ Org
Resource Rendezvous
Virtual BUS
Service Discovery
Resource Manipulation
CRUDN
Sensing Acting
Physical
Network
Service
Platform
Service Profile 1
(Connected Health)
Service Profile 2
(Connected Edu)
Service Profile 3
(Connected Car)
Service Profile 4
(Connected Retail)
Service Profile 5
(Smart City)
SIP
SSDP
Model/ JSON

## Slide 34: Internet & IoT layer comparison
sensing, acting
OIC, oneM2M, CoAP
DTN
v6
6LowPAN…
WiFi, BLE, VANET...
fiber, radio, light...
email, web, phone...
WWW, HTTP, URL
TCP UDP
IP
ND, ARP…
Ethernet, sonet...
copper fiber radio...
Internet
IoT
Service layer
Network
[from Internet Hourglass model by Steve Deering]

## Slide 35: (background) Service layer – oneM2M
oneM2M Layered Model
Common Services Functions
[From TS0001 Functional Architecture, oneM2M]

## Slide 36: (background) Service layer – oneM2M
[Cisco presentation at IoT World Forum 2013]

## Slide 37: (background) oneM2M & Cisco comparison
oneM2M Layered Model
Network
Service layer

## Slide 38: OIC Functional Block Diagram
Transport
Networking
L2 Connectivity
Application profiles
Connected Health
Smart Home
Automotive
Retail
OIC Framework
Device management
Group management
Protocol bridge/ Gateway
Messaging
Streaming
Discovery
Security
ID & Addressing
CRUDN
Resource model

## Slide 39: OIC Framework – IoT Platform(?)
Transport
Networking
L2 Connectivity
Application profiles
Connected Health
Smart Home
Automotive
Retail
OIC Framework
Device management
Group management
Protocol bridge/ Gateway
Messaging
Streaming
Discovery
Security
ID & Addressing
CRUDN
Resource model

## Slide 40: OIC Framework – IoT Platform(?)
OIC Framework
Device management
Group management
Protocol bridge/ Gateway
Messaging
Streaming
Discovery
Security
ID & Addressing
CRUDN
Resource model
ID & Address
Identifier & locator with resolution scheme
Security
Authentication, & Access control & Encryption
Resource management
Define resource & management
Create, Retrieve, Update, Delete & Notification of Resource
Messaging
Transfer a message with control method
Streaming
Deliver data flow with QoS constraints
Discovery
Finding relevant device & service information
Device management
Manage device capability
Group management
Manage group & collective group activity
Protocol bridge
Intermediate or translate between different protocols

## Slide 41: OIC Framework – IoT Platform(?)
mDNS, DNS-SD
TCP, UDP, DTN
Homenet, Anima
CoAP, http
IPv6, 6lo, geonet
URI, UUID, IPv6
IBE, DTLS/TLS
BT/ BLE, 802.15.4, 802.11p
oneM2M TS0001, ooo4
XMPP, MQTT
Smart Object

## Slide 42: OIC Framework – IoT Platform(?)
mDNS, DNS-SD
TCP, UDP, DTN
Homenet, Anima
CoAP, http
IPv6, 6lo, geonet
URI, UUID, IPv6
IBE, DTLS/TLS
BT/ BLE, 802.15.4, 802.11p
oneM2M TS0001, ooo4
XMPP, MQTT
Smart Object

## Slide 43: OIC specification summary
Spec items | Summary | Issues
ID & Addressing | Entity to identify: Resource, Device, App, User? | Define entities to identify Define ID per entity Identifier format: URI (URN+URL) Present a resolution scheme
 | IDs per an entity: UUID & URI | 
 | ID format: UUID, URI = <host>/datapath/? | 
 | Resolution scheme | 
Resource model | Resource terms: attributes, interface… | Clarify resource terms & rules Common resource & attributes Align with existing resource standard (oneM2M)
 | Resource format | 
 | Common resource & attributes | 
CRUDN | Generic Request & Response format | Parameters for REQ & RES Generic procedure (Notification)
 | CRUDN procedures with Request & Response | 
Discovery | Local: mDNS, or CoAP based | Multiprotocol: mDNS vs CoAP discovery Advance remote discovery Define a registration standard Term: Search & Advertisement (?)
 | Remote: TBD | 
 | Registration | 
 | Unsolicited (Search & Advertisement) | 
Messaging | CoAP, HTTP, MQTT,XMPP | REST transaction with MQTT Multi-protocol: CoAP & MQTT CoAP over BT/ BLE
 | Non-IP support (CoAP over BT./BLE) | 
Streaming | Uni-directional streaming(?) TBD | Streaming with REST model
Device mgmt | On boarding, ii) configuration, iii) device monitoring & iv) diagnostics | OMA LWM2M? Resource model conflict?
Group mgmt | Collection with collective action | Align with open source
Protocol bridge | CoAP to Foo bridge(?) | Align with open source & ii) spec item?
Security | Provisioning, Authentication, Access Control | Align with ID & Addressing

## Slide 44: (tentative) OIC protocol stack
Smart Device
APP |  |  |  |  |  |  | 
REST |  |  |  |  |  |  | 
HTTP | MQTT | XMPP | DDS | RTP | CoAP | mDNS | SSDP
TCP |  |  |  | UDP |  |  | 
IPv4/ IPv6 |  |  |  |  |  |  | 
L2 Connectivity |  |  |  |  |  |  | 
Thin device (IP)
APP |  |  | 
REST |  |  | 
CoAP | mDNS | SSDP | MQTT
UDP |  |  | 
IPv4/ IPv6 |  |  | 
L2 Connectivity |  |  | 
Thinner device (non-IP)
APP Profile + (CoAP?) | 
GAP, GATT | 
SMP | ATT
L2CAP | 
Link Layer | 
BT Baseband + RF | 
APP Profile + (CoAP?) | 
GAP, GATT | 
SMP | ATT
L2CAP | 
Link Layer | 
BT Baseband + RF | 

## Slide 45: (tentative) OIC protocol stack
Smart Device
APP |  |  |  |  |  |  | 
REST |  |  |  |  |  |  | 
HTTP | MQTT | XMPP | DDS | RTP | CoAP | mDNS | SSDP
TCP |  |  |  | UDP |  |  | 
IPv4/ IPv6 |  |  |  |  |  |  | 
L2 Connectivity |  |  |  |  |  |  | 
Thin device (IP)
APP |  |  | 
REST |  |  | 
CoAP | mDNS | SSDP | MQTT
UDP |  |  | 
IPv4/ IPv6 |  |  | 
L2 Connectivity |  |  | 
Thinner device (non-IP)
APP Profile + (CoAP?) | 
GAP, GATT | 
SMP | ATT
L2CAP | 
Link Layer | 
BT Baseband + RF | 
APP Profile + (CoAP?) | 
GAP, GATT | 
SMP | ATT
L2CAP | 
Link Layer | 
BT Baseband + RF | 

## Slide 46: Appendix

## Slide 47: Network Architecture
“A set of principles and basic mechanisms that guide network engineering.”
  Boundaries fuzzy: bounded from “above” by requirements and from “below” by engineering.
  Even fuzzier: boundary between architecture and mechanism.
Historically, informal architectural ideas guided design of the Internet protocols, but the architecture was formalized later...
  “The Design Philosophy of the DARPA Internet Protocols”, David D. Clark, SIGCOMM ‘88, p.106.

## Slide 48: Architecture, a conceptual metaphor

## Slide 49: Network Architecture
What entities are named, and how?
How do naming, addressing, and routing inter-relate?
Where & how is state installed and removed?
How are functions modularized?
How are resources allocated?
How are security boundaries drawn and enforced?

## Slide 50: A brief history of Internet
1960s: the idea of packet switching
  Paul Baran (RAND) & Donald Davies (NPL) & Leonard Kleinrock (MIT)
1969: Birth of the ARPANET packet-switched network.
  First IMP installed at UCLA
1974: Cerf/Kahn paper on internetworking
  Many elements of the final Internet protocol design
1977: ARPA research program on internetworking
  Important players included: BBN, DEC, ISI, MIT, SRI, UCLA
  6 prototype implementations of TCP/IP
Jan 1, 1983: Birth of the Internet
  ARPAnet switched to TCP/IP protocols; Mil Std.
~1991: World-Wide Web introduced
  From academic tool to popular culture

## Slide 51: phone system
The Phone System is not about phones, it’s about dynamically constructing a path from caller to callee, connecting wires to other wires.
Data can’t flow until a path is set up so efficiency decreases when setup time or holding time decreases, not suitable for computer network with “bursty” nature.

## Slide 52: packet switching
Change viewpoint to focus on endpoints rather than paths.
Data sent in independent chunks and each chunk contains the name of the final destination.
(Transitivity) If node gets a chunk for a different destination, forward it to the next hop.
Paul Baran & Donald Davies & Leonard Kleinrock
In 1964 these ideas were ‘lunatic fringe’ - anyone who knew anything about communications knew this could never work.

## Slide 53: ARPANET
Bob Taylor had an idea of connecting computers (1966)
  “Computer as a Communication Device” with J.P. Licklider (1968)
Larry Roberts led ARPANET project with packet switching idea
Wes Clark put forth an idea of ‘Router’
  BBN built an IMP with Honeywell computer
First IMP installed at UCLA (1969)
Bob Taylor & Larry Roberts
No host-to-host protocol
NWG (Network Working Group)
  The birth of IETF & RFC
NCP (Network Control Protocol)
  Host-to-host protocol 1970
Remote log-in & file transfer

## Slide 54: TCP/ IP
Packet switching worked so well that by 1973 there appeared multiple networks.
Each was done as a clean slate so they didn't interoperate.
  Needs a network of networks
Vint Cerf & Bob Kahn realized that a common encapsulation & addressing structure could glue together arbitrary networks.
  First demo in 77 & ARPANET switches to TCP/ IP from NCP in 83
Vint Cerf & Bob Kahn in 70s

## Slide 55: Top level goals
develop an effective technique for multiplexed utilization of existing interconnected networks.
  Network (subnets): components which were to be interconnected to provide some larger service.
  originally aim to connect ARPANET with ARPA packet radio network.
An alternative(?): design a unified system which incorporated a variety of different transmission media, a multi-media network.

## Slide 56: Thin waist
A universal internetworking protocol IP forms a “common bearer service” end-to-end.
a single internet protocol to maximize interoperability & minimize number of service interfaces
a narrow internet protocol to assume least common network functionality to maximize number of usable networks

## Slide 57: Some changes
Internet was invented in this word for resource sharing. Since then many changes occurred.
  New devices: PC, cellular, machine & sensor
  New technology: wireless & optical
  New applications: multimedia, real-time, p2p, emergency
  New requirements: mobility, robustness & security