## Slide 1: OCF Core Technology, aka IoT platform OCF 1.0
June 2017
JinHyeock Choi, jinchoe@samsung.com

## Slide 2: Contents
IoT overview
  Main challenges
OCF Architecture
  Functional Block Diagram & OCF Framework
Resource model
  Resource, Resource Type, Device
RESTful Transaction
  CRUDN, Messaging, Discovery
Bridging
  Content-Negotiation, Bridging

## Slide 3: Contents
IoT overview
  Main challenges
OCF Architecture
  Functional Block Diagram & OCF Framework
Resource model
  Resource, Resource Type, Device
RESTful Transaction
  CRUDN, Messaging, Discovery
Bridging
  Content-Negotiation, Bridging

## Slide 4: Internet of Things
Real World Internet
M2M
Ubiquitous Computing
Web of Thing
Cyber Physical System
Internet of Everything
WSN
Industrial Internet

## Slide 5: Internet
User
Human
Cyber World
Cyber World open to Human
Digital

## Slide 6: Internet of Things?
User
Physical World
Human
Cyber World
Cyber & Physical World integrated & open to Human
Digital
Physical
Cyber World open to Human

## Slide 7: RESTful Architecture Style
Client
Server
Request
Response
CRUD & N operation
Resource (representation)
Resource (representation)
Addressable resources
A uniform, constrained interface
Representation based manipulation
Communicate statelessly
Hypermedia State Engine
REST Architecture Style
{
"n": "myRoomTemperature",
"rt": "oic.r.temperature",
"if": "oic.if.a",
"id": "example_id_xyz",
"temperature": 23,
"units": "C",
"setValue": 25
}
Physical entity
Entity handler
RESTful Architecture (Representational State Transfer)
  Resource based operation
    Real world ‘entity’ is represented as ‘Resource’
  Resource manipulation via Request/ Response: CRUDN

## Slide 8: (conceptual) IoT Architecture & Procedures
User
Device
Sensor
Sensor
Actuator
Gateway
Service Server
Actuator

## Slide 9: (conceptual) IoT Architecture & Procedures
User
Device
Sensor
Sensor
Actuator
Gateway
Service Server
Actuator
Controlling & Monitoring
with sensor & actuator

## Slide 10: Main IoT challenges
User
Device
Sensor
Sensor
Actuator
Gateway
Service Server
Actuator
Networked Embedded Device
Connectivity
IoT Network
IoT Core Framework
Big Data Analysis
UX
IoT Security

## Slide 11: Contents
IoT overview
  Main challenges
OCF Architecture
  Functional Block Diagram & OCF Framework
Resource model
  Resource, Resource Type, Device
RESTful Transaction
  CRUDN, Messaging, Discovery
Bridging
  Content-Negotiation, Bridging

## Slide 12: RESTful Architecture Style
Client
Server
Request
Response
CRUD & N operation
Resource (representation)
Resource (representation)
Addressable resources
A uniform, constrained interface
Representation based manipulation
Communicate statelessly
Hypermedia State Engine
REST Architecture Style
{
"n": "myRoomTemperature",
"rt": "oic.r.temperature",
"if": "oic.if.a",
"id": "example_id_xyz",
"temperature": 23,
"units": "C",
"setValue": 25
}
Physical entity
Entity handler
RESTful Architecture (Representational State Transfer)
  Resource based operation
    Real world ‘entity’ is represented as ‘Resource’
  Resource manipulation via Request/ Response: CRUDN

## Slide 13: OCF Device: Roles
OCF Device
  a logical entity that assumes one or more Roles (e.g., Client, Server)
Roles
  Client:
    initiate an transaction (send a request) & access a server to get a service
  Server:
    host resources & send a response & provide service
  Intermediary:
    Process a REST message & Provide support to deliver messages between Client & Server (?).
Server
Client
Intermediary
OCF Device
OCF Device
OCF Device
Server

## Slide 14: Logical organization: 3 part approach
[OIC Concepts & Architecture Review, Ravi Subramaniam]
OIC Client
CoAP
Device:
“Wrist Band”
Request
Response
Time: 11:30
Rate: 80
Name: Ravi HR
Representation
URI: /s/hm/data
GET
Protocol
Servlet
Resource Type
Resource
/s/hm/data
Relative URI
/192.168.1.1/s/hm/mgmt
Fully-qualified URI
Resolution: I
Range: I
Name: S
Time: UT
Rate: F
Name: S
Resource Interface
Resource model
Communication and Interoperability
(Protocol processing
& Messaging)
Resource model and organization
(Declarative)
Device abstraction (entity handler)
(Imperative)
RESTful transaction
Abstraction
Resource model
OIC Server
Binding
Resource Address
Resource
Entity Handler
Entity (e.g. HW Sensor)
RESTful transaction
Abstraction

## Slide 15: IoT Protocol Stacks
15
OPEN CONNECTIVITY FOUNDATION MEMBER CONFIDENTIAL INFORMATION
DMC R&D Center ⓒ 2013 SAMSUNG Electronics Co.
6loWPAN
IPv6
6tisch
6lo
RFC 4862
RFC 4861
16ng
RFC 6459
ETSI TS102859
IEEE 802.3 Ethernet
IEEE 802.11 WiFi
IEEE 802.15.1 Bluetooth
IEEE 802.15.7 VLC
IEEE 802.15.4 Zigbee
IEEE 1901.2 PLC
IEEE 802.11 p C2C-CC
IEEE 802.16 WiMAX
Cellular 3GPP LTE
IP over Foo (PLC, VLC)
Geo-Networking
Energy Efficient Protocol
Delay Tolerant Transport
RPL
6light
homenet
eman
Ad-hoc VANET
Proxy/ Gateway
MIB
TCP
UDP
QUIC
SCTP
RTP
ICMP
Access Control
AAA
EAP
DIAMETER
SSL/TLS
HTTP/ HTTPS
CoAP
MQTT
XMPP
DDS
DNS
Resource Abstract
URI/ ID
Meta data /Link
Resource Representation
Attributes
Structure/ Org
Resource Rendezvous
Virtual BUS
Service Discovery
Resource Manipulation
CRUDN
Sensing Acting
Physical
Network
Service
Platform
Service Profile 1
(Connected Health)
Service Profile 2
(Connected Edu)
Service Profile 3
(Connected Car)
Service Profile 4
(Connected Retail)
Service Profile 5
(Smart City)
SIP
SSDP
Model/ JSON

## Slide 16: Internet & IoT layer comparison
sensing, acting
OCF, oneM2M, CoAP
DTN
v6
6LowPAN…
WiFi, BLE, VANET...
fiber, radio, light...
email, web, phone...
WWW, HTTP, URL
TCP UDP
IP
ND, ARP…
Ethernet, sonet...
copper fiber radio...
Internet
IoT
Network
[from Internet Hourglass model
by Steve Deering]
Resource/Service layer

## Slide 17: OCF Functional Block Diagram
{
"n": MyRoomLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a“],
"id": "b.switch_TF38_3",
"value": "true"
}
Transport
Networking
L2 Connectivity
Application profiles
Connected Health
Smart Home
Automotive
Industry
OCF Framework
ID & Addressing
Resource model
CRUDN
Messaging
Discovery
Device management
Security
Group management
Bridging
Streaming(?)
Vertical profile
Common
IoT functions or
OCF Core features,
IoT Platform(?)

## Slide 18: OCF Functional Block Diagram
Transport
Networking
L2 Connectivity
Application profiles
Connected Health
Smart Home
Automotive
Industry
OCF Framework
ID & Addressing
Resource model
CRUDN
Messaging
Discovery
Device management
Security
Group management
Bridging
Streaming(?)
CoAP, HTTP
TCP, UDP, DTN
Homenet, Anima
URI, UUID, IPv6
IPv6, 6lo, geonet
mDNS, DNS-SD
IBE, DTLS/TLS
oneM2M TS0001, ooo4
XMPP, MQTT
BT/ BLE, 802.15.4, 802.11p
Smart Object

## Slide 19: OCF Functional Block Diagram: WG/TGs
Transport
Networking
L2 Connectivity
Application profiles
Connected Health
Smart Home
Automotive
Industry
OCF Framework
ID & Addressing
Resource model
CRUDN
Messaging
Discovery
Device management
Security
Group management
Bridging
Streaming(?)
Smart Home TG
Core Framework TG
Security WG

## Slide 20: OCF Functional Block Diagram: WG/TGs
Transport
Networking
L2 Connectivity
Application profiles
Connected Health
Smart Home
Automotive
Industry
OCF Framework
ID & Addressing
Resource model
CRUDN
Messaging
Discovery
Device management
Security
Group management
Bridging
Streaming(?)
Smart Home Project
Architecture TG
Security WG
Cloud support (?)
Automotive Project
Industrial TG
BLE-GATT
Project
CoAP Native Cloud Project
Bridging TG
JOOE Project
WiFi Easy
Setup Project
Healthcare Project

## Slide 21: OCF Framework: IoT Platform(?)
Transport
Networking
L2 Connectivity
Application profiles
Connected Health
Smart Home
Automotive
Retail
OCF Framework
ID & Addressing
Resource model
CRUDN
Messaging
Discovery
Device management
Security
Group management
Bridging
Streaming(?)

## Slide 22: OCF Framework: IoT Platform(?)
OCF Framework
Resource model
CRUDN
Device management
Group management
Bridging
Streaming
Messaging
Security
ID & Addressing
Transport
Networking
L2 Connectivity
Discovery
Application profiles
Connected Health
Smart Home
Automotive
Retail

## Slide 23: OCF Framework – IoT Platform?
OCF Framework
Group management
Bridging
Streaming
Device management
Security
Discovery
Messaging
ID & Addressing
CRUDN
Resource model
Identifier & locator for OCF entities with resolution scheme
Realizing CRUDN with transfer protocol (e.g., CoAP, HTTP, MQTT, DDS)
A way to construct Resource with attributes, Resource Type & Link.
Create, Retrieve, Update, Delete & Notification of Resource with generic Request & Response.
Manage device capability, configuration, monitoring and life cycle management.
Onboarding, Authentication, Authorization & Access control
Finding relevant device & service information. Pull or Push based & Direct & Indirect
Manage group & collective group activity, Group/ Scene/ Script/ Rule
Intermediate or translate between different echo, protocols. Bridging with Virtual entity with synchronization
Deliver data flow with QoS constraints.

## Slide 24: Core features & issues
Status
Core features | Sub-items | Status | Issues
ID & Addressing | Entity to identify: Resource, Device, App, User? |  | Define entities to identify Define identifier/Name per entity Identifier format: URI (URN+URL) Alignment with SHP, MSC, Mobile Present a resolution scheme
 | IDs per an entity: URI = URN + URL |  | 
 | ID format: UUID, URI? |  | 
 | Resolution scheme |  | 
Resource model | Resource terms: attributes, interface… |  | Clarify resource terms & rules Common resource & attributes Align with SHP or existing resource standard (oneM2M)
 | Resource structure: Link, Colleciton |  | 
 | Common resource & attributes |  | 
CRUDN | Generic Request & Response format |  | Parameters for REQ & RES Generic procedure (Notification)
 | CRUDN procedures with Request & Response |  | 
Discovery | Local: mDNS, or CoAP based |  | Multiprotocol: mDNS vs CoAP discovery Advance remote discovery Define a registration standard Term: Search & Advertisement (?)
 | Remote: TBD |  | 
 | Registration |  | 
 | Unsolicited (Search & Advertisement) |  | 
Messaging | CoAP, HTTP, MQTT |  | REST transaction with MQTT Multi-protocol: CoAP & MQTT CoAP over BT/ BLE
 | Non-IP support (CoAP over BT./BLE) |  | 
Streaming | Uni-directional streaming(?) TBD |  | Streaming with REST model
Device mgmt | On boarding, ii) configuration, iii) device monitoring & iv) diagnostics |  | OMA LWM2M? Resource model conflict?
Group mgmt | Collection with collective action |  | Align with open source
Protocol bridge | CoAP to Foo bridge(?) |  | Align with open source & ii) spec item?
Security | Provisioning, Authentication, Access Control |  | Align with ID & Addressing
mature
developing
Not started

## Slide 25: Current status
Status
Spec items | Sub-items | Status | Issues
ID & Addressing | ocf URI |  | No resolution scheme specified
Resource model | Resource, Properties, Resource Type |  | Collection CRUDN unspecified Interface still unclear (i.e. Interface as filter) Query needs further specification
 | Link & Collection |  | 
 | Interface |  | 
 | Query |  | 
CRUDN | CRUDN procedures with generic REQ & RES |  | Parameters for REQ & RES
Discovery | CoAP based discovery (Endpoint, Resource) |  | Random delay for CoAP multicast RD selection & publishing needs elaboration
 | Resource directory |  | 
Messaging | coap |  | CoAP over TCP needs further works Version options number assignment
 | coap+tcp |  | 
Device mgmt | On boarding & Provisioning, ii) configuration, iii) Diagnostics & maintenance |  | On boarding & Provisioning in SecWG Configuration in 11.2 with oic.wk.con Maintenance in 11.5 with oic.wk.mnt Is it adequate?
Group mgmt | Group/Scene/Script/Rule |  | Only scene specified
Bridging (?) | Versioning and Content-Negotiation |  | 
 | Bridging |  | /oic/res swagger(?)
mature
developing
Not started

## Slide 26: Contents
IoT overview
  Main challenges
OCF Architecture
  Functional Block Diagram & OCF Framework
Resource model
  Resource, Resource Type, Device
RESTful Transaction
  CRUDN, Messaging, Discovery
Bridging
  Content-Negotiation, Bridging

## Slide 27: Resource (instance)
Resource:
  "Resource" means a specific "resource instance".
Resource features: a resource is determined with the following features.
  URI
    In general, a resource can have any URI but some special resources have pre-defined URI.
  Property
    <Key: Value> pairs which characterize the resource.
  OCF Link
    establish a relationship among resources.
/resource1URI
Property 1 <key1: value1>
Property 2 <key2: value2>
Typed Web link
/resource2URI
Property 3 <key3: value3>
Property 4 <key4: value4>
link

## Slide 28: Resource (instance)
Resource:
  "Resource" means a specific "resource instance".
Resource features: a resource is determined with the following features.
  URI
    In general, a resource can have any URI but some special resources have pre-defined URI.
  Property
    <Key: Value> pairs which characterize the resource.
  OCF Link
    establish a relationship among resources.
/myLightSwitch
{
"n": MyRoomLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"]
"id": "b.switch_TF38_3",
"value": true
}

## Slide 29: Property
Property specification
  Property is “key-value” pair characterizing Resource Type & specified with the following table with 8 columns.
Property title | Property name | Value type | Value rule | Mandatory | Access mode | Unit | Description
Name | n | string | recommended that the length be restricted to 64 characters (UTF-8)) | Mandatory | Read Only |  | Human friendly name of a resource (e.g., “n”: “MyLivingRoomLight”)
Ex) Name (“n”) property specification
Quiz
What is the difference between “property name” & “name property”?
What is the name property name?
What is the name property title?

## Slide 30: Resource Type: Format
Resource Type is a class or category of Resources & specified with
i) The table for Resource Type & ii) The table for associated properties
Ex) “Binary Switch” Resource Type Specification
Property title | Property name | Value type | Value rule | Unit | Access mode | Mandatory | Description
Name | n | string |  |  | R | No | Human friendly name For example, “My Light Switch”
Resource Type ID | rt | string |  |  | R | yes | Represent a specific resource type.
Interface | if | string |  |  | R | Yes | Unique identifier for device (UUID)
Value | value | Boolean |  |  | RW | yes | Status of the switch
Binary switch properties
fixed URI | Resource Type Title | Resource Type ID (“rt” value) | interfaces | Description | Related Functional Interaction | M/CM/O
none | Binary switch | oic.r.switch.binary | oic.if.a, oic.if.baseline | Binary switch to turn on-off the device to which it’s associated. | Actuation | O

## Slide 31: OCF Link: Typed Web Link
Type web link (RFC 5988) which is a means of expressing connections between resources.
Context URI: indicate the resource determining the relationship context. (e.g. /myRoom)
Target URI: indicate the resource determining the relationship target. (e.g. /myLight)
Relation: a relationship from the context URI to target URI. (e.g. "inside" )
Attributes: a set of attributes that provide metadata about the target URI. (e.g. “rt“)
{
"Context URI": /myRoom,
"Target URI": /myLgith,
"relationship": "inside",
"resource type for target URI": "oic.r.light"
}
(conceptual) example) of Typed Web link
from room to light

## Slide 32: OCF Link
OCF Link consist of Parameters which are key-value pairs characterize link relationship.
anchor: context URI. when present, the hosting Device ID. When absent, hosting Resource.
href: target URI, mandatory
rel: relationship, the default value of “hosts” when absent
rt: Resource Type ID of the target Resource, mandatory
if: The Interfaces which the target Resource supports, mandatory
p: bitmap indicating discoverabiliy & observability of target resource
eps: Endpoints (i.e., IP address + port #) with which the target Resource can be accessed.
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rel": "hosts",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}

## Slide 33: Collection: Resource structure
Flat structure among Resources
  No hierarchy among Resources, no sub-Resource & Resource are organized with Link
Collection
  A Resource with OCF Links
    “links” Property with an array of OCF Links as its value.
{
"rt": ["oic.wk.col"],
"if": ["oic.if.ll", "oic.if.baseline", "oic.if.b"],
"links": [
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myFanSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:a::b1d4]:33333"}]
}
]
}

## Slide 34: Interface
Defines interaction constraints on a Resource
  Which properties are exposed
  Which methods are allowed: retrieve-only or updateable
  How links are processed: oic.if.b
  Application semantics –
    for example oic.if.s and oic.if.a for sensors and actuators vs. oic.if.r and oic.if.rw for status and configuration parameters
Interface Title | Interface ID | Applicable Methods | Description
baseline | “oic.if.baseline” | RETRIEVE, UPDATE | Access to all the Properties, Retrieves all the Properties.
links list | “oic.if.ll” | RETRIEVE | Access to OCF Links & retrieves the array of Links
batch | “oic.if.b” | RETRIEVE, UPDATE | Interact with a collection of Resources at the same time.
read-only | “oic.if.r” | RETRIEVE | exposes the Properties of a Resource that may be ‘read’.
read-write | “oic.if.rw” | RETRIEVE, UPDATE | exposes only those Properties that may be both ‘read’ and “written”
actuator | “oic.if.a” | CREATE, RETRIEVE, UPDATE | The actuator Interface is used to read or write the Properties of an actuator Resource.
sensor | “oic.if.s” | RETRIEVE | The sensor Interface is used to read the Properties of a sensor Resource.

## Slide 35: Query: “rt” & “if” query
“if” query specifies to indicate the “interface” to use
  POST /exampleCollectionURI?if=oic.if.b
“rt” query specified as a filter
{
"rt": ["oic.wk.col"],
"if": ["oic.if.ll", "oic.if.baseline", "oic.if.b"],
"links": [
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myFanSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:a::b1d4]:33333"}]
}
]
}
GET /collection
?rt=oic.r.switch.binary
RESPONSE
[ {
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}, ]
REQUEST

## Slide 36: Core Resources
Core Resources
  ATG defines several Resource Types which are common to all verticals.
fixed URI | Resource Type Title | Resource Type ID (“rt” value) | interfaces | Description | Related Functional Interaction | M/CM/O
/oic/res | Default | oic.wk.res | oic.if.ll, oic.if.baseline | expose the Resources hosted by the responding Server and facilitate OCF Device discovery. | Discovery | M
/oic/d | Device | oic.wk.d | oic.if.r, oic.if.baseline | expose the Property of logical OCF Device (e.g., Device Type). | Discovery | M
/oic/p | Platform | oic.wk.d | oic.if.r, oic.if.baseline | expose the Property of physical platform. | Discovery | M
Application profiles
OCF Framework
Core Resource 1
Core Resource 2
Core Resource 2
Vertical Resource 1
Vertical Resource 1

## Slide 37: Core Resources: Examples
{
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"di": "dc70373c-1e8d-4fb3-962e-017eaa863989",
"icv": "ocf.1.0.0",
"dmv": "ocf.res.1.0.0, ocf.sh.1.0.0",
"piid": "6F0AAC04-2BB0-468D-B57C-16570A26AE48"
}
{
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"links": [
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/res",
"rel": "self",
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:a::b1d4]:33333"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/d",
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/p",
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightBrightness",
"rt": ["oic.r.brightness"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}
]
}
{
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"pi": "54919CA5-4101-4AE4-595B-353C51AA983C",
"mnmn": "STRK, Inc"
}
/oic/res
/oic/d
/oic/p

## Slide 38: OCF Device
OIC device is specified
  with i) core resources & ii) device specific resources.
    Device type specified by “oic.d.<device type>”, (e.g., oic.d.light)
  For example “light device (oic.d.light)” shall have mandatory
    Core resources: ① /oic/res, ② /oic/d, ③ /oic/p,
    Device specific resources: ④ Binary switch (oic.r.switch.binary), ⑤ Brightness (oic.r.light.brightness)
Device Title | Device Type | Associated Resource Type | M/CM/O
Light | oic.d.light | /oic/res (oic.wk.res) | M
 |  | /oic/d (oic.wk.d, oic.d.light) | M
 |  | /oic/p (oic.wk.p) | M
 |  | Binary switch (oic.r.swtich.binary) | M
 |  | Brightness (oic.r.light.brightness) | O
Example: Smart light device with 5 resources
oic/d
oic/p
Binary switch
Brightness
oic/res

## Slide 39: Device example: light device (oic.d.light)
{
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"links": [
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/res",
"rel": "self",
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:a::b1d4]:33333"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/d",
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/p",
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightBrightness",
"rt": ["oic.r.brightness"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}
]
}
{
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"n": "myDeskLamp",
"di": "dc70373c-1e8d-4fb3-962e-017eaa863989",
"icv": "ocf.1.0.0",
"dmv": "ocf.res.1.0.0, ocf.sh.1.0.0",
"piid": "6F0AAC04-2BB0-468D-B57C-16570A26AE48"
}
{
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"n": "myDeskLampBrightness",
"brightness": 50
}
{
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"n": "myDeskLampSwitch",
"value": true
}
/oic/res
/oic/d
{
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"pi": "54919CA5-4101-4AE4-595B-353C51AA983C",
"mnmn": "STRK, Inc"
}
/oic/p
/myDeskLampSwitch
/myDeskLampBrightness

## Slide 40: Discovery procedure with oic/res
{
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"pi": "54919CA5-4101-4AE4-595B-353C51AA983C",
"mnmn": "STRK, Inc"
}
{
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"n": "myDeskLampSwitch",
"value": true
}
{
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"n": "myDeskLampBrightness",
"brightness": 50
}
{
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"n": "myDeskLamp",
"di": "dc70373c-1e8d-4fb3-962e-017eaa863989",
"icv": "ocf.1.0.0",
"dmv": "ocf.res.1.0.0, ocf.sh.1.0.0",
"piid": "6F0AAC04-2BB0-468D-B57C-16570A26AE48"
}
{
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"links": [
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/res",
"rel": "self",
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:a::b1d4]:33333"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/d",
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/p",
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightBrightness",
"rt": ["oic.r.brightness"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}
]
}
GET /oic/res
RESPONSE
Device discovery with “oic/res”
  A response to “oic/res” carries device type in “rt” of “oic/d” in addition to all resource information.
[
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/res",
"rel": "self",
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:a::b1d4]:33333"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/d",
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/p",
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightBrightness",
"rt": ["oic.r.brightness"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}
]

## Slide 41: Contents
IoT overview
  Main challenges
OCF Architecture
  Functional Block Diagram & OCF Framework
Resource model
  Resource, Resource Type, Device
RESTful Transaction
  CRUDN, Messaging, Discovery
Bridging
  Content-Negotiation, Bridging

## Slide 42: CRUDN: generic operation procedure
Client
Server
Request
Response
CRUD & N operation

## Slide 43: CRUDN: generic operation procedure
CREATE
RETRIEVE
UPDATE
DELETE
NOTIFICATION
  Subscribed notification
    Client makes a priori subscription for a target resource of interest (e.g., CoAP observe)
  Unsubscribed notification
    No a priori subscription for the target resource (e.g., Fire alarm or VANET emergency
  New way of Request & Response needed.

## Slide 44: Generic Request & Response message
(tentative) Request message parameter/ Operation | 
Operation (op) | operation to be executed, i.e. CRUD&N(?)
Subscription indication (observe opt?) | Request to notify upon resource state change
To (to) | The identifier (URI) of the target resource for the operation
From (fr) | the identifier of the message Originator in URI (ex) Device ID, Client ID or APP ID
Request Identifier (ri) | uniquely identifies a Request message
Content (cn) | contents (resource representation) to be transferred
Request expiration Timestamp (ot) (?) | Till when the message is valid (?)
(tentative) Response message parameter/ Results | 
Operation (op) (?) | operation to be executed, i.e. N
Response Code (rs) | successful, unsuccessful, Unsolicited N (?)
To (to) | the identifier of the message Originator, ‘fr’ in the matching request or multicast address in case of unsubscribed notification
From (fr) | The identifier of the target resource, ‘to’ in the matching request or the identifier or message originator in case of unsubscribed notification.
Request Identifier (ri) | uniquely identifies a Request message (or a priori fixed value)
Content (cn) | contents (resource representation) to be transferred
Response Expiration Timestamp (ot)? | when the request message expires

## Slide 45: Messaging: CoAP
CRUDN with CoAP methods
  No one-to-one correspondence between CRUDN & POST/PUT/GET/DELETE.
CRUDN vs POST/PUT/GET/DELETE methods
  CREATE with POST or PUT
  RETRIEVE with GET
  UPDATE with POST or PUT
  DELETE with DELETE
  NOTIFY with GET
  (partial) UPDATE with PATCH

## Slide 46: Messaging: CRUDN with CoAP method
CREATE with POST:
  i) Existing target URI for the resource responsible for creation & ii) the URI of the new resource is determined by the server, forwarded to the client.
CREATE with PUT:
  i) Non existing target URI for the new resource to be created.
UPDATE with POST:
  i) Existing target URI for the resource to be updated & ii) incorporation of the payload with the existing resource (i.e., partial update)
UPDATE with PUT:
  i) Existing target URI for the resource to be updated & ii) whole replacement with the payload.

## Slide 47: CREATE with POST
CREATE with POST: i) Existing target URI for the resource responsible for creation & ii) the URI of the new resource is determined by the server, forwarded to the client.
POST /existingURI
OIC server
/existingURI
/newURI
{
"n": MyRoomFoo",
"rt": "oic.r.foo",
"if": "oic.if.a",
“value": “True”
}
{
"n": MyRoomFoobar",
"rt": "oic.r.foobar",
"if": "oic.if.a",
“number": 100
}
{
"n": MyRoomFoobar",
"rt": "oic.r.foobar",
"if": "oic.if.a",
“number": 100
}

## Slide 48: CREATE with POST
CREATE with POST: i) Existing target URI for the resource responsible for creation & ii) the URI of the new resource is determined by the server, forwarded to the client.
RESPONSE
OIC server
/existingURI
/newURI
{
"n": MyRoomFoo",
"rt": "oic.r.foo",
"if": "oic.if.a",
“value": “True”
}
{
"n": MyRoomFoobar",
"rt": "oic.r.foobar",
"if": "oic.if.a",
“number": 100
}
with /newURI
{
"n": MyRoomFoobar",
"rt": "oic.r.foobar",
"if": "oic.if.a",
“number": 100
}

## Slide 49: CREATE with PUT
CREATE with PUT: i) Non existing target URI for the new resource to be created.
PUT /newURI
OIC server
/newURI
{
"n": MyRoomFoobar",
"rt": "oic.r.foobar",
"if": "oic.if.a",
“number": 100
}
{
"n": MyRoomFoobar",
"rt": "oic.r.foobar",
"if": "oic.if.a",
“number": 100
}

## Slide 50: CREATE with PUT
RESPONSE
OIC server
/newURI
{
"n": MyRoomFoobar",
"rt": "oic.r.foobar",
"if": "oic.if.a",
“number": 100
}
CREATE with PUT: i) Non existing target URI for the new resource to be created.

## Slide 51: UPDATE with POST
UPDATE with POST: i) Existing target URI for the resource to be updated & ii) incorporation of the payload with the existing resource (i.e., partial update).
POST /existingURI
OIC server
{
"value": false
}
/existingURI
{
"n": MyRoomFoo",
"rt": "oic.r.foo",
"if": "oic.if.a",
"value": true
}

## Slide 52: UPDATE with POST
POST /existingURI
OIC server
/existingURI
{
"n": MyRoomFoo",
"rt": "oic.r.foo",
"if": "oic.if.a",
"value": false
}
{
"value": false
}
UPDATE with POST: i) Existing target URI for the resource to be updated & ii) incorporation of the payload with the existing resource (i.e., partial update).

## Slide 53: UPDATE with PUT
UPDATE with PUT: i) Existing target URI for the resource to be updated & ii) whole replacement with the payload.
PUT /existingURI
OIC server
/existingURI
{
"n": MyRoomFoo",
"rt": "oic.r.foo",
"if": "oic.if.a",
"value": true
}
{
"value": false
}

## Slide 54: UPDATE with PUT
UPDATE with PUT: i) Existing target URI for the resource to be updated & ii) whole replacement with the payload.
PUT /existingURI
OIC server
/existingURI
{
"value": false
}
{
"value": false
}

## Slide 55: UPDATE with PATCH
PATCH /existingURI
OIC server
/existingURI
{
"foo": [{"A": 1}, {"B": 2}],
"bar": [{"C": 3}, {"D": 4}]
}
[
{
"op": "replace",
"path": "foo/1",
"value": {"A": 5}
},
{
"op": "add",
"path": "bar/1",
"value": {"E": 6}
}
]
UPDATE with PATCH: i) Existing target URI for the resource to be updated & ii) more minute& precise manipulation with PATCH document with “op” (add, replace, remove), “path”, “value”.

## Slide 56: UPDATE with PATCH
PATCH /existingURI
OIC server
/existingURI
{
"foo": [{"A": 5}, {"B": 2}],
"bar": [{"E": 6}, {"C": 3}, {"D": 4}]
}
[
{
"op": "replace",
"path": "foo/1",
"value": {"A": 5}
},
{
"op": "add",
"path": "bar/1",
"value": {"E": 6}
}
]
UPDATE with PATCH: i) Existing target URI for the resource to be updated & ii) more minute& precise manipulation with PATCH document with “op” (add, replace, remove), “path”, “value”.

## Slide 57: Discovery
Direct vs Indirect discovery
  Direct communication between discovering & discovered devices.
  3rd party assisted discovery
Pull vs Push based discovery
  Pull: a discovering device requests to discovered devices.
  Push: a discovered device advertises to discovering devices.
Current OCF discovery
  CoAP discovery: direct & pull based
  Resource Directory: indirect & pull based

## Slide 58: (Direct) Discovery with oic/res
Discovery with multicast GET to “oic/res”
  A Client sends multicast GET to /oic/res &
  All the Servers send back the responses with the device type and all the hosted Resource Links.
Multicast GET to /oic/res
coap://[ff02::158]:5683/oic/res
Response with
Resource & Device information

## Slide 59: (Direct) Discovery with oic/res
{
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"pi": "54919CA5-4101-4AE4-595B-353C51AA983C",
"mnmn": "STRK, Inc"
}
{
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"n": "myDeskLampSwitch",
"value": true
}
{
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"n": "myDeskLampBrightness",
"brightness": 50
}
{
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"n": "myDeskLamp",
"di": "dc70373c-1e8d-4fb3-962e-017eaa863989",
"icv": "ocf.1.0.0",
"dmv": "ocf.res.1.0.0, ocf.sh.1.0.0",
"piid": "6F0AAC04-2BB0-468D-B57C-16570A26AE48"
}
{
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"links": [
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/res",
"rel": "self",
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:a::b1d4]:33333"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/d",
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/p",
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightBrightness",
"rt": ["oic.r.brightness"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}
]
}
GET /oic/res
RESPONSE
Discovery with multicast GET to “oic/res”
  A Client sends multicast GET to /oic/res &
  All the Servers send back the responses with the device type and all the hosted Resource Links.
[
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/res",
"rel": "self",
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:a::b1d4]:33333"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/d",
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/p",
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightBrightness",
"rt": ["oic.r.brightness"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}
]

## Slide 60: (Direct) Discovery with oic/res
{
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"pi": "54919CA5-4101-4AE4-595B-353C51AA983C",
"mnmn": "STRK, Inc"
}
{
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"n": "myDeskLampSwitch",
"value": true
}
{
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"n": "myDeskLampBrightness",
"brightness": 50
}
{
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"n": "myDeskLamp",
"di": "dc70373c-1e8d-4fb3-962e-017eaa863989",
"icv": "ocf.1.0.0",
"dmv": "ocf.res.1.0.0, ocf.sh.1.0.0",
"piid": "6F0AAC04-2BB0-468D-B57C-16570A26AE48"
}
{
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"links": [
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/res",
"rel": "self",
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:a::b1d4]:33333"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/d",
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/p",
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightBrightness",
"rt": ["oic.r.brightness"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}
]
}
GET /oic/res?rt=oic.d.light
RESPONSE
[
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/res",
"rel": "self",
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:a::b1d4]:33333"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/d",
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/p",
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightBrightness",
"rt": ["oic.r.brightness"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}
]
Discovery with multicast GET to “oic/res”
  A Client sends multicast GET to /oic/res &
  All the Servers send back the responses with the device type and all the hosted Resource Links. With query parameter, only specific type of Device or Resource can be retrieved.

## Slide 61: (Direct) Discovery with oic/res
{
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"pi": "54919CA5-4101-4AE4-595B-353C51AA983C",
"mnmn": "STRK, Inc"
}
{
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"n": "myDeskLampSwitch",
"value": true
}
{
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"n": "myDeskLampBrightness",
"brightness": 50
}
{
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"n": "myDeskLamp",
"di": "dc70373c-1e8d-4fb3-962e-017eaa863989",
"icv": "ocf.1.0.0",
"dmv": "ocf.res.1.0.0, ocf.sh.1.0.0",
"piid": "6F0AAC04-2BB0-468D-B57C-16570A26AE48"
}
{
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"links": [
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/res",
"rel": "self",
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:a::b1d4]:33333"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/d",
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/p",
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightBrightness",
"rt": ["oic.r.brightness"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}
]
}
GET /myDeskLampSwitch
RESPONSE
{
"value": true
}
Discovery with multicast GET to “oic/res”
  A Client sends multicast GET to /oic/res &
  All the Servers send back the responses with the device type and all the hosted Resource Links. With query parameter, only specific type of Device or Resource can be retrieved.
  Each Resource can be retrieved for further information.

## Slide 62: (Direct) Discovery with oic/res
Discovery with multicast GET to “oic/res”
  A Client sends multicast GET to /oic/res &
  All the Servers send back the responses with the device type and all the hosted Resource Links. With query parameter, only specific type of Device or Resource can be retrieved.
  Each Resource can be retrieved for further information.
{
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"pi": "54919CA5-4101-4AE4-595B-353C51AA983C",
"mnmn": "STRK, Inc"
}
{
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"n": "myDeskLampSwitch",
"value": true
}
{
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"n": "myDeskLampBrightness",
"brightness": 50
}
{
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"n": "myDeskLamp",
"di": "dc70373c-1e8d-4fb3-962e-017eaa863989",
"icv": "ocf.1.0.0",
"dmv": "ocf.res.1.0.0, ocf.sh.1.0.0",
"piid": "6F0AAC04-2BB0-468D-B57C-16570A26AE48"
}
{
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"links": [
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/res",
"rel": "self",
"rt": ["oic.wk.res"],
"if": ["oic.if.ll", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:a::b1d4]:33333"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/d",
"rt": ["oic.wk.d", "oic.d.light"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/oic/p",
"rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightBrightness",
"rt": ["oic.r.brightness"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}
]
}
GET /myDeskLampSwitch
?if=oic.if.baseline
RESPONSE
{
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"n": "myDeskLampSwitch",
"value": true
}

## Slide 63: (Indirect) Discovery with Resource Directory
Resource Directory definition
  An OCF Device facilitating indirect discovery by exposing 3rd party Resources (i.e. Links) via /oic/res using mandatory “oic.wk.rd” Resource Type.
Publishing
Device
Resource
Directory
Response
Discover
3rd party Resource via RD
GET /oic/res
Response
Publish a Resource Link
POST /oic/rd

## Slide 64: (Indirect) Discovery with Resource Directory
Resource Directory definition
  An OCF Device facilitating indirect discovery by exposing 3rd party Resources (i.e. Links) via /oic/res using mandatory “oic.wk.rd” Resource Type.
RD features
  RD discovery
    Discover an RD and select one via oic.wk.rd
  Resource publish
    publish/update/delete Resource (i.e. Links) via /oic/res of an RD using oic.wk.rd
  Resource expose
    Expose published Resources via /oic/res of RD

## Slide 65: RD: oic.wd.rd specification
“oic.wk.rd” Resource Type Specification
“oic.wk.rd” Properties
Property title | Property name | Value type | Value rule | Unit | Access mode | Mandatory | Description
Selector | sel | Integer or JSON Object |  |  | R | Yes | Provides the criteria for RD selection. Either JSON Object describing the selection criteria (e.g. Power) specified in 11.3.6.2.2.1 or an integer representing a bias factor calculated by RD. The value is in the range of 0 to 100 - 0 implies that RD is not to be selected. Client chooses RD with highest bias factor or randomly between RDs that have same bias factor.
fixed URI | Resource Type Title | Resource Type ID (“rt” value) | interfaces | Description | Related Functional Interaction | M/CM/O
/oic/rd | Resource Directory | oic.wk.rd | oic.if.baseline | The discoverable Resource Type through with which an RD 1) facilitates its discovery and provides the criteria to select an RD and 2) allows OCF Devices to publish, update and delete their Links in /oic/res of the RD. An OCF Device can find the presence of oic.wk.rd to discover an RD, then sends GET request to /oic/rd to acquire the selection criteria. An OCF Device can send POST request with Links in its payload to expose those Links in /oic/res of the RD. Also OCF Device can send DELTE request with suitable query (e.g. “di” or “ins”) to remove its Links from /oic/res of the RD. | Discovery | CM for RD

## Slide 66: RD discovery
GET /oic/res?rt=oic.wk.rd
Resource Directory
/oic/res
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]}
]
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
/oic/res response

## Slide 67: RD select
GET /oic/rd
Resource Directory
/oic/res
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]}
]
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
/oic/rd response
{
"rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"],
"sel": 50
}

## Slide 68: Resource publish
POST /oic/rd
Resource Directory
/oic/res
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]}
]
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
{
"di": "88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49 ",
"links": [
{
"anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [
{"ep": "coaps://[fe80::b1d6]:22222"}]},
"ttl": 600
}

## Slide 69: Resource publish
POST /oic/rd
Resource Directory
/oic/res
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch", "rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d6]:22222"}],
"ins": 11235 }
]
POST response
{
"di": "88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"links": [
{
"anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [
{"ep": "coaps://[fe80::b1d6]:22222"}],
"ins": 11235},
"ttl": 600
}

## Slide 70: Resource update
POST /oic/rd
Resource Directory
/oic/res
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
{
"di": "88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49 ",
"links": [
{
"anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [
{"ep": "coaps://[fe80::b1d6]:1111"}],
"ins": 11235},
"ttl": 600
}
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch", "rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d6]:22222"}],
"ins": 11235 }
]

## Slide 71: Resource update
Resource Directory
POST /oic/rd
/oic/res
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch", "rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d6]:1111"}],
"ins": 11235 }
]
POST response
{
"di": " 88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"links": [
{
"anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [
{"ep": "coaps://[fe80::b1d6]:1111"}],
"ins": 11235},
"ttl": 600
}

## Slide 72: Resource delete
DELETE?ins=11235
Resource Directory
/oic/res
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch", "rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d6]:1111"}],
"ins": 11235 }
]

## Slide 73: Resource delete
DELETE?ins=11235
Resource Directory
/oic/res
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]}
]

## Slide 74: Resource delete
DELETE?ins=11235
Resource Directory
/oic/res
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Publishing
Device
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]}
]
DELETE response: success

## Slide 75: Resource expose
GET /oic/res
Resource Directory
/oic/res
/oic/rd
{"rt": ["oic.wk.rd"], "if": ["oic.if.baseline"],
"sel": 50 }
Discovering
Device
/oic/res response
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch", "rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d6]:1111"}],
"ins": 11235 }
]
[
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/d", "rt": ["oic.wk.d", "oic.d.bridge"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/p", "rt": ["oic.wk.p"],
"if": ["oic.if.r", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}] },
{ "anchor": "ocf://e61c3e6b-9c54-4b81-8ce5-f9039c1d04d9",
"href": "/oic/rd", "rt": ["oic.wk.rd"],
"if": ["oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d4]:11111"}]},
{ "anchor": "ocf://88b7c7f0-4b51-4e0a-9faa-cfb439fd7f49",
"href": "/myLightSwitch", "rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"], "p": {"bm": 3},
"eps": [{"ep": "coaps://[fe80::b1d6]:1111"}],
"ins": 11235 }
]

## Slide 76: Contents
IoT overview
  Main challenges
OCF Architecture
  Functional Block Diagram & OCF Framework
Resource model
  Resource, Resource Type, Device
RESTful Transaction
  CRUDN, Messaging, Discovery
Bridging
  Content-Negotiation, Bridging

## Slide 77: multi-Resource model support
Several IoT standard under development
  Would be better for OCF to be able to interoperate with them
RESTful based
  with common transfer & connectivity solution: CoAP over IP
  any Client & Server can exchange Request & Response messages
Different resource models defined: OCF, oneM2M, IPSO
  Difficulty understanding resource representation in payload
Client
Server
Request
Response

## Slide 78: Versioning: content-negotiation
A way to indicate one’s resource model would help alignment
  Each Client/ Server is able to indicate which resource model it supports.
Versioning: resource model indication
  a new media type for OIC resource model, for example, application/vnd.ocf+cbor (10,000)
  register the media type in IANA
  Use Accept & Content-Format option to indicate the resource model
Client
Server
Req: GET /thermostat: Accept (application/vnd.ocf+cbor)
Res: 2.05 Content-Format (application/vnd.ocf+cbor)

## Slide 79: Versioning: content-negotiation
CoAP Option Number | Name | Format | Length (bytes)
2049 | Accept Version | unit | 2
2053 | Content-Format Version | unit | 2
A way to indicate one’s resource model would help alignment
  Each Client/ Server is able to indicate which resource model it supports.
Versioning: resource model indication
  a new media type for OIC resource model, for example, application/vnd.ocf+cbor (10,000)
  register the media type in IANA
  Use Accept & Content-Format option to indicate the resource model
New CoAP Options
version | Accept or Content-Format Option |  | Accept or Content-Format Version Option | 
 | Media Type | ID | OCF version | 
OIC 1.1 | application/cbor | 60 |  | 
OCF 1.0 | application/vnd.ocf+cbor | 10000 | 1.0.0 | 2048
OCF Content-Format

## Slide 80: Versioning: Differentiated responses
In case of multiple Content-Format support, a server sends back a response in proper resource model.
GET /collection Accept:application/vnd.ocf+cbor (10000)
RESPONSE
[
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myFanSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}
]
REQUEST
/collection
{
"rt": ["oic.wk.col"],
"if": ["oic.if.ll", "oic.if.baseline", "oic.if.b"],
"links": [
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myFanSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}
]
}
OCF 1.0 Server
OCF 1.0 Client

## Slide 81: Versioning: Differentiated responses
In case of multiple Content-Format support, a server sends back a response in proper resource model.
GET /collection
Accept: application/cbor (60)
RESPONSE
{
"links": [
{
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3, "sec": true, "port": 22222},
},
{
"href": "/myFanSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3, "sec": true, "port": 22222},
}
]
}
REQUEST
/collection
{
"rt": ["oic.wk.col"],
"if": ["oic.if.ll", "oic.if.baseline", "oic.if.b"],
"links": [
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myLightSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
},
{
"anchor": "ocf://dc70373c-1e8d-4fb3-962e-017eaa863989",
"href": "/myFanSwitch",
"rt": ["oic.r.switch.binary"],
"if": ["oic.if.a", "oic.if.baseline"],
"p": {"bm": 3},
"eps": [{"ep": "coaps://[2001:db8:b::c2e5]:22222"}]
}
]
}
OCF 1.0 Server
OIC 1.1 Client

## Slide 82: OCF Bridge: technical approach
OIC device (client)
OCF Bridge Device
OCF Light Device
OCF Fan Device
Entity
Entity
An approach would be to represent
  ① the hub device as OCF bridge device &
  ② non- OCF bridged devices as OCF virtual devices.
The non-OCF devices are manipulated by interacting with the corresponding OCF virtual devices within OCF bridge device.
  Entity handlers ensure that virtual OIC devices & physical devices are synchronized.

## Slide 83: OCF Bridge: operation sketch with OCF & oneM2M
Bridge in between
  which plays the role of both OCF & oneM2M entities.
Separation of OCF & oneM2M operation
  The intermediary, i.e., Bridge, interact with OIC (& oneM2M) devices with OIC (& oneM2M) procedures respectively.
OCF device
(controller)
① OCF REQ
oneM2M device
(sensor & actuator)
Bridge
② oneM2M REQ
③ oneM2M RES
④ OCF RES
(virtual)
OCF device
(virtual)
oneM2M device
OCF and oneM2M resource translation

## Slide 84: Appendix

## Slide 85: Main IoT Technical Challenges vs Internet
Networked Embedded Device
Big Data Analysis
IoT Network
UX
IoT Core Framework
IoT Standard
IoT Security 기술
Sensor
Sensor
Service Server
Gateway
Actuator
Actuator
Connectivity
User
Device
Web server
LAN, WLAN
TCP/ IP
WWW
Search (?)
IPSec, DES
Web Browser
IETF & W3C & IEEE & 3GPP

## Slide 86: Main IoT Technical Challenges vs Internet
Networked Embedded Device
Big Data Analysis
IoT Network
UX
IoT Core Framework
IoT Standard
IoT Security 기술
Sensor
Sensor
Service Server
Gateway
Actuator
Actuator
Connectivity
User
Device
Web server
LAN, WLAN
TCP/ IP
WWW
Search (?)
IPSec, DES
Web Browser
IETF & W3C & IEEE & 3GPP
SUN
3Com
Cisco
NETSCAPE
Google
RSA
Apple

## Slide 87: (Example) NEST Operations with Protocols
NEST Thermostat
(Sensor & Actuator)
NEST
Service Server
Gateway
Monitoring with NEST thermostat (by Smartphone)
Smart Phone

## Slide 88: (Example) NEST Operations with Protocols
Smart Phone
NEST Thermostat
(Sensor & Actuator)
NEST
Service Server
Gateway
Monitoring with NEST thermostat (by Smartphone)
0. Event occurrence
1. Request NEST for temperature
1.1. data format with JSON
1.2. message & method with HTTP GET
1.3. delivery with TCP/IP
1.4. over the air with WiFi

## Slide 89: (Example) NEST Operations with Protocols
Smart Phone
NEST Thermostat
(Sensor & Actuator)
NEST
Service Server
Gateway
0. Event occurrence
1. Request NEST for temperature
1.1. data format with JSON
1.2. message & method with HTTP GET
1.3. delivery with TCP/IP
2. Response with temperature
1.4. over the air with WiFi
Monitoring with NEST thermostat (by Smartphone)
Simplified & further procedures needed
service discovery & ID resolution
lightweight network protocol
access control & security
et cetra…

## Slide 90: (Example) NEST Operations with Protocols
Smart Phone
NEST Thermostat
(Sensor & Actuator)
Gateway
Controlling with NEST thermostat (by NEST Service Server)
0. Event occurrence
NEST
Service Server

## Slide 91: (Example) NEST Operations with Protocols
Smart Phone
NEST Thermostat
(Sensor & Actuator)
NEST
Service Server
Gateway
Controlling with NEST thermostat (by NEST Service Server)
0. Event occurrence
1. Request NEST for temperature change
1.1. data format with JSON
1.2. message & method with HTTP PUT
1.3. delivery with TCP/IP
2. Change temperature with HVAC
1.4. over the air with WiFi

## Slide 92: (Example) NEST Operations with Protocols
Smart Phone
NEST Thermostat
(Sensor & Actuator)
NEST
Service Server
Gateway
Controlling with NEST thermostat (by NEST Service Server)
0. Event occurrence
1. Request NEST for temperature change
1.1. data format with JSON
1.2. message & method with HTTP PUT
1.3. delivery with TCP/IP
2. Change temperature with HVAC
1.4. over the air with WiFi
3. Response with state info
Simplified & further procedures needed
service discovery & ID resolution
lightweight network protocol
access control & security
et cetra…